## Slide 1: On-Demand Dynamic Software Analysis
Joseph L. Greathouse
Ph.D. Candidate
Advanced Computer Architecture Laboratory
University of Michigan
December 12, 2011
Notes: This talk was given for the AMD Tech Topics series on December 12, 2011. (Thanks to Matthew Stringer and Martin Pohlack). This is basically a mix of my ISCA2011 talk along with some very preliminary slides from my ASPLOS 2012 talk. See the ISCA slides for detailed notes of what all the animations mean.

## Slide 2: Software Errors Abound
NIST: SW errors cost U.S. ~$60 billion/year as of 2002
FBI CCS: Security Issues $67 billion/year as of 2005
  >⅓ from viruses, network intrusion, etc.
Cataloged Software Vulnerabilities
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008
CVE Candidates | 1246 | 1587 | 2434 | 1596 | 2769 | 4889 | 7245 | 6743 | 7291
CERT Vulnerabilities | 1090 | 2437 | 4129 | 3784 | 3780 | 5990 | 8064 | 7236 | 8077

## Slide 3: Hardware Plays a Role
In spite of proposed solutions
Hardware Data Race Recording
Deterministic Execution/Replay
Atomicity Violation Detectors
Bug-Free Memory Models
Bulk Memory Commits
TRANSACTIONAL
MEMORY
IBM BG/Q
AMD ASF?

## Slide 4: Example of a Modern Bug
Thread 2
mylen=large
Thread 1
mylen=small
ptr
∅
Nov. 2010 OpenSSL Security Flaw
if(ptr == NULL) {
len=thread_local->mylen;
ptr=malloc(len);
memcpy(ptr, data, len);
}

## Slide 5: Example of a Modern Bug
if(ptr==NULL)
if(ptr==NULL)
memcpy(ptr, data2, len2)
ptr
LEAKED
TIME
Thread 2
mylen=large
Thread 1
mylen=small
∅
len2=thread_local->mylen;
ptr=malloc(len2);
len1=thread_local->mylen;
ptr=malloc(len1);
memcpy(ptr, data1, len1)

## Slide 6: Dynamic Software Analysis
Analyze the program as it runs
  System state, find errors on any executed path
  LARGE runtime overheads, only test one path
Developer
Instrumented Program
In-House
Test Machine(s)
LONG run time
Analysis Results
Analysis Instrumentation
Program

## Slide 7: Runtime Overheads: How Large?
Taint Analysis (e.g.TaintCheck)
Dynamic Bounds Checking
Data Race Detection (e.g. Inspector XE)
Memory Checking (e.g. MemCheck)
2-200x
10-80x
5-50x
2-300x
Symbolic Execution
10-200x

## Slide 8: Could use Hardware
Data Race Detection: HARD, CORD, etc.
Taint Analysis: Raksha, FlexiTaint, etc.
Bounds Checking: HardBound
None Currently Exist; Bugs Are Here Now
Single-Use Specialization
  Won’t be built due to HW, power, verification costs
  Unchangeable algorithms locked in HW

## Slide 9: Goals of this Talk
Accelerate SW Analyses Using Existing HW
Run Tests On Demand: Only When Needed
Explore Future Generic HW Additions

## Slide 10: Outline
Problem Statement
Background Information
  Demand-Driven Dynamic Dataflow Analysis
Proposed Solutions
  Demand-Driven Data Race Detection
  Unlimited Hardware Watchpoints

## Slide 11: Example Dynamic Dataflow Analysis
a += y
z = y * 75
y = x * 1024
w = x + 42
Check w
Check w
validate(x)
x = read_input()
Clear
a += y
z = y * 75
y = x * 1024
x = read_input()
Propagate
Associate
Input
Check a
Check a
Check z
Check z
Data
Meta-data

## Slide 12: Demand-Driven Dataflow Analysis
Only Analyze Shadowed Data
Native
Application
Instrumented Application
Instrumented
Application
Meta-Data Detection
Non-Shadowed Data
Shadowed Data
No meta-data

## Slide 13: Finding Meta-Data
No additional overhead when no meta-data
  Needs hardware support
Take a fault when touching shadowed data
Solution: Virtual Memory Watchpoints
V→P
V→P
FAULT

## Slide 14: Results by Ho et al.
From “Practical Taint-Based Protection using Demand Emulation”
System | Slowdown (normalized)
Taint Analysis | 101.7x
On-Demand Taint Analysis | 1.98x

## Slide 15: Outline
Problem Statement
Background Information
  Demand-Driven Dynamic Dataflow Analysis
Proposed Solutions
  Demand-Driven Data Race Detection
  Unlimited Hardware Watchpoints

## Slide 16: Software Data Race Detection
Add checks around every memory access
Find inter-thread sharing events
Synchronization between write-shared accesses?
  No? Data race.

## Slide 17: Data Race Detection
Thread 2
mylen=large
Thread 1
mylen=small
if(ptr==NULL)
if(ptr==NULL)
len1=thread_local->mylen;
ptr=malloc(len1);
memcpy(ptr, data1, len1)
len2=thread_local->mylen;
ptr=malloc(len2);
memcpy(ptr, data2, len2)
Shared?
Synchronized?
TIME

## Slide 18: SW Race Detection is Slow
Chart: Race Detector Slowdown (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean | blackscholes | bodytrack | facesim | ferret | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
 | 48.1483 | 98.4291 | 261.2096 | 278.4874 | 121.3327 | 28.0403 | 23.5499 | 83.2106 | 28.465 | 119.353 | 103.9687 | 80.0587 | 123.4686 | 5.3481 | 65.9072 | 137.1643 | 164.4939 | 109.1232 | 36.2791 | 99.1297 | 207.8853 | 74.7261
Phoenix
PARSEC

## Slide 19: Inter-thread Sharing is What’s Important
“Data races ... are failures in programs that access and update shared data in critical sections” – Netzer & Miller, 1992
if(ptr==NULL)
if(ptr==NULL)
len1=thread_local->mylen;
ptr=malloc(len1);
memcpy(ptr, data1, len1)
len2=thread_local->mylen;
ptr=malloc(len2);
memcpy(ptr, data2, len2)
Thread-local data
NO SHARING
Shared data
NO INTER-THREAD SHARING EVENTS
TIME

## Slide 20: Very Little Inter-Thread Sharing
Phoenix
PARSEC
Chart: % Write-Sharing Events
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | blackscholes | bodytrack | facesim | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster
 | 7.9849e-05 | 0.001152 | 2.3676e-05 | 8.4683e-06 | 1.9398e-05 | 7.4788e-05 | 0.024552 | 0.00036515 | 1.2408 | 0.24109 | 0.60989 | 0.00067053 | 0.22956 | 0.086346 | 0.54613 | 0.48584 | 0.19271 | 2.884 | 0.18591

## Slide 21: Use Demand-Driven Analysis!
Multi-threaded
Application
Software Race Detector
Software Race Detector
Local Access
Inter-thread sharing
Inter-thread Sharing Monitor

## Slide 22: Finding Inter-thread Sharing
Virtual Memory Watchpoints?
  ~100% of accesses cause page faults
Granularity Gap
Per-process not per-thread
Must go through the kernel on faults
Syscalls for setting/removing meta-data
FAULT
FAULT
Inter-Thread Sharing

## Slide 23: Hardware Sharing Detector
HITM in Cache: W→R Data Sharing
Hardware Performance Counters
Read Y
S
I
S
I
HITM
Core 1
Core 2
Write Y=5
M
Y=5
Pipeline
Cache
0
0
0
0
Perf. Ctrs
1
1
-1
FAULT
-
-
-
-
PEBS
Armed
Debug Store
EFLAGS
EIP
RegVals
MemInfo
Precise
Fault

## Slide 24: Potential Accuracy & Perf. Problems
Limitations of Performance Counters
  HITM only finds W→R Data Sharing
  Hardware prefetcher events aren’t counted
Limitations of Cache Events
  SMT sharing can’t be counted
  Cache eviction causes missed events
  False sharing, etc…
PEBS events still go through the kernel

## Slide 25: On-Demand Analysis on Real HW
Execute Instruction
SW Race Detection
Enable Analysis
Disable Analysis
HITM
Interrupt?
Sharing Recently?
Analysis
Enabled?
NO
NO
NO
YES
YES
YES
> 97%
< 3%

## Slide 26: Performance Difference
Chart: Race Detector Slowdown (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean | blackscholes | bodytrack | facesim | ferret | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
 | 48.1483 | 98.4291 | 261.2096 | 278.4874 | 121.3327 | 28.0403 | 23.5499 | 83.2106 | 28.465 | 119.353 | 103.9687 | 80.0587 | 123.4686 | 5.3481 | 65.9072 | 137.1643 | 164.4939 | 109.1232 | 36.2791 | 99.1297 | 207.8853 | 74.7261
 | 6.2238 | 12.141 | 16.6407 | 5.4552 | 10.7669 | 8.8601 | 4.3034 | 8.344 | 5.44 | 15.5475 | 21.3128 | 24.1851 | 9.1784 | 3.3791 | 29.8428 | 58.3285 | 134.5787 | 34.272 | 17.0509 | 53.7348 | 168.5864 | 25.228
Phoenix
PARSEC

## Slide 27: Performance Increases
Chart: Demand-driven Analysis Speedup (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean | blackscholes | bodytrack | facesim | ferret | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
 | 7.7361 | 8.1072 | 15.697 | 51.0497 | 11.269 | 3.1648 | 5.4724 | 9.9724 | 5.2325 | 7.6767 | 4.8782 | 3.3103 | 13.4522 | 1.5827 | 2.2085 | 2.3516 | 1.2223 | 3.184 | 2.1277 | 1.8448 | 1.2331 | 2.962
Phoenix
PARSEC
51x

## Slide 28: Demand-Driven Analysis Accuracy
Chart: Demand-driven Analysis Speedup (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean | blackscholes | bodytrack | facesim | ferret | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
 | 7.7361 | 8.1072 | 15.697 | 51.0497 | 11.269 | 3.1648 | 5.4724 | 9.9724 | 5.2325 | 7.6767 | 4.8782 | 3.3103 | 13.4522 | 1.5827 | 2.2085 | 2.3516 | 1.2223 | 3.184 | 2.1277 | 1.8448 | 1.2331 | 2.962
1/1
2/4
3/3
4/4
3/3
4/4
4/4
2/4
4/4
4/4
2/4
Accuracy vs. Continuous Analysis: 97%

## Slide 29: Outline
Problem Statement
Background Information
  Demand-Driven Dynamic Dataflow Analysis
Proposed Solutions
  Demand-Driven Data Race Detection
  Unlimited Hardware Watchpoints

## Slide 30: Watchpoints Globally Useful
Byte/Word Accurate and Per-Thread

## Slide 31: Watchpoint-Based Software Analyses
Taint Analysis
Data Race Detection
Deterministic Execution
Canary-Based Bounds Checking
Speculative Program Optimization
Hybrid Transactional Memory

## Slide 32: Challenges
Some analyses require watchpoint ranges
  Better stored as base + length
Some need large # of small watchpoints
  Better stored as bitmaps
Need a large number

## Slide 33: The Best of Both Worlds
Store Watchpoints in Main Memory
Cache watchpoints on-chip

## Slide 34: Demand-Driven Taint Analysis
Chart: Slowdown (x)
| 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parse | 252.eon | 253.perlbmk | 254.gap | 255.vortex | 256.bzip2 | 300.twolf | GeoMean
MINEMU | 2.428 | 1.979 | 4.292 | 2.306 | 3.199 | 2.411 | 2.294 | 3.461 | 3.526 | 3.4 | 2.3 | 2.048 | 2.7206
Umbra | 2.553 | 3.298 | 4.834 | 3.486 | 7.027 | 4.08 | 5.652 | 6.817 | 6.597 | 7.145 | 3.799 | 2.79 | 4.5479
Watchpoint | 1.0115 | 1.0015 | 1.0025 | 1.0087 | 1 | 1.0057 | 1.3227 | 1.037 | 1.0449 | 21.521 | 1.0159 | 1.0052 | 0 | 1.3364

## Slide 35: Watchpoint-Based Data Race Detection
Chart: Speedup (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean
RC+Bitmap | 5.9939 | 10.1362 | 17.0605 | 3.9246 | 26.8364 | 6.3221 | 7.0108 | 9.0149
Chart: 
| blackscholes | bodytrack | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
RC+Bitmap | 19.5295 | 5.4979 | 5.4919 | 3.1904 | 24.2608 | 11.5603 | 13.3685 | 2.1128 | 0.99697 | 12.008 | 5.7608 | 6.5957
Phoenix
PARSEC

## Slide 36: Watchpoint Deterministic Execution
Chart: Performance vs Grace
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean
RC+Bitmap | 0.98811 | 0.77569 | 0.99769 | 0.54391 | 0.90913 | 0.99958 | 0.84571 | 0.84965
Chart: 
| 312.swim_m | 316.applu_m | 318.galgel_m | 320.equake_m | 324.apsi_m | 326.gafort_m | 328.fma3d_m | 330.art_m | 332.ammp_m | GeoMean
RC+Bitmap | 0.93686 | 0.87829 | 0.85315 | 0.97898 | 0.99888 | 0.97764 | 0.9752 | 0.99979 | 0.42196 | 0.85556
Phoenix
SPEC OMP2001

## Slide 37: BACKUP SLIDES