## Slide 1: A Power Characterization and Management of GPU Graph Traversal
ADAM MCLAUGHLIN*, INDRANI PAUL†, JOSEPH GREATHOUSE†, SRILATHA MANNE†, AND SUDHKAHAR YALAMANCHILI*
*GEORGIA INSTITUTE OF TECHNOLOGY
†AMD RESEARCH
Notes: Brad will update the title slide

## Slide 2: Motivation
Future machines may not be able to run at full power
  Expensive
    Installations consume tens of Megawatts
  Dark Silicon
  Current SoCs prevent damaging hotspots and maintain thermal limits
All of the Top 10 machines from the Green 500 leverage GPUs
Practical applications are constrained by power or thermal limitations
The HPC community does not want to sacrifice performance for power
It’s critical to develop power management techniques for emergent irregular applications on GPUs
Notes: Adam: Not enough room on this slide to mention the focus on graph algorithms, hence use of the term “irregular applications” instead for the last bullet. Slides 3-4 clarify what that term means (i.e. graph algorithms and how they’re used to solve real-world problems).

## Slide 3: Graph Algorithms
Irregular Applications
  Typically memory bound
  Inconsistent memory access patterns
  Characteristics unknown at compile time
  Interesting data sets are massive
Graph structures – Not a one size fits all problem
  Scale-free
  Small world
  Road networks
  Meshes
Notes: Scale-free the degree of the vertices follow a power-law distribution. Seen in social networks and the internet.
Small world is where a graph is highly connected so the diameter of graph is logarithmic to the number of vertices.

## Slide 4: Applications of Graph Algorithms
Machine Learning
Compiler Optimization
  Register allocation
  Points-to Analysis
Social Network Analysis
Computational Biology
Computational Fluid Dynamics
Urban Planning
Path finding
Notes: Points-to analysis is alises analysis

## Slide 5: Breadth-First Search
Choose a source node to start from
Explore neighbors of
  Explore neighbors of neighbors, and so on
Building block to more complicated problems
  Betweenness Centrality
  All-pairs Shortest Paths
  Strongly Connected Components
  “Bricks and Mortar” of classical graph algorithms
Especially useful for parallel graph algorithms
  Depth-First Search is P-Complete
Notes: P-complete algorithms are known to be hard to parallelize

## Slide 6: Recent work on BFS
SHOC Benchmark Suite
  Quadratic [Harish and Narayanan HiPC ‘07]
    Naively assign a thread to every vertex on every iteration
    Lots of unnecessary memory fetches and branch overhead
  Linear with atomics [Luo, Wong, and Hwu DAC ‘10]
    Asymptotically Optimal O(m + n) work
      For graphs with n vertices and m edges
    Fastest publicly available OpenCL implementation
    Used for the experiments in this paper
Linear with prefix sums [Merrill, Garland, and Grimshaw PPoPP ‘12]
  Fastest GPU implementation
Direction-Optimizing [Beamer, Asanović, and Patterson SC’12]
Notes: May not need to cover each bullet in detail.

## Slide 7: Change in Parallelism Over Time
Two trends
  Few BFS iterations that process many nodes each
    Scale-free, small world
  Many BFS iterations that process few nodes each
    Road networks, sparse meshes
Notes: Time can vary between ms and 100s of ms. It depends the on the critical path of the traversal.
In_2004 input and copaper_citeseer are an examples of small world and/or scale free. The line between the two is blurry, but slightly more scale free.
The black read and blue are just different starting vertex.

## Slide 8: Experimental Setup
How do we leverage this information to manage power?
  Two “knobs” of control
    DVFS state
    Number of active Compute Units (CUs)
A10-5800K Trinity APU
  384 Radeon Cores
    6 SIMD Units
    16 Lanes with 4-way VLIW
  3 DVFS States
    High: 800 MHz, 1.275V
    Medium: 633 MHz, 1.2V
    Low: 304 MHz, 0.9375V
  18 Manageable Power States
    Up to 6 Active SIMDs (Compute Units)
    3 DVFS States

## Slide 9: Power Measurements
Measure GPU power directly
  Receive estimates from power management firmware
  Sample power every millisecond
Overhead of changing DVFS state ~ microseconds
Analyze power configurations offline
  Limitations in changing power states during execution
Throughput Baseline
  Low Frequency
  4 Active CUs
Latency Baseline
  Medium Frequency
  2 Active CUs

## Slide 10: Distinguishing Power and Energy
Our goal is to maximize performance in a power-constrained environment
Our goal is NOT to minimize energy
  “Race to idle” is not a valid solution
Notes: National lab LINPACK – Call from the power company

## Slide 11: Benchmark Graphs
Name | Vertices | Edges | Significance
coPapersCiteseer | 434,102 | 16,036,720 | Social Network
delaunay_n23 | 8,388,608 | 25,165,784 | Random Triangluation
asia.osm | 11,950,757 | 12,711,603 | Street Network
ldoor | 952,203 | 22,785,136 | Sparse Matrix
af_shell10 | 1,508,065 | 25,582,130 | Sheet Metal Forming
kkt_power | 2,063,494 | 6,482,320 | Nonlinear Optimization
rgg_n_2_22_s0 | 4,194,304 | 30,359,198 | Random Geometric Graph
G3_circuit | 1,585,478 | 3,037,674 | AMD Circuit Simulation
hugebubbles_00020 | 21,198,119 | 31,790,179 | 2D Dynamic Simulations
in-2004 | 1,382,908 | 13,591,473 | Web Crawl
packing_500x100x100-b050 | 2,145,852 | 17,488,243 | Fluid Mechanics
Notes: Training set: hugebubbles and copapers
These input sets come from many different areas
Delauanay and rgg are synthetic, the rest are real

## Slide 12: Static Oracle
Given a graph and power cap, determine the best power state
  Exhaustively run all settings
  Pick the setting that has…
    …the least execution time
    …instantaneous power within the cap at all times
  Refer to this setting as the static oracle
    “Static” because the same power setting is used throughout the traversal

## Slide 13: Best Configuration Varies with Graph Input
Consider an 82.18% Power Cap
  Left (delaunay_n23): Medium Frequency and 6 CUs
  Right (G3_Circuit): High Frequency and 5 CUs

## Slide 14: Leveraging Both Degrees of Freedom
Sometimes it is better to boost frequency than CUs (af)
Sometimes it is better to boost CUs than frequency (del)
Boost both degrees somewhat rather than boosting one maximally (in)
Reduce one degree to be able to boost the other (pack)
Notes: These 4 represent the four different types of behaviors.

## Slide 15: An Algorithmic Approach
How to determine the best configuration for a given graph and power cap?
Intuition: Graphs tend to be more sensitive to either latency or parallelism
  Use simple, offline, graph metrics to determine this sensitivity
    Number of nodes
    Average degree
  Diameter would be ideal, but that requires too much preprocessing
Notes: Standard deviation requires too much preprocessing as well

## Slide 16: Clustering
Red circles: training set
Blue x’s: Classified via K-means clustering
High average degree implies a high potential for load imbalances
  Scale-free, small world graphs
Low average degree means more uniform work
  Meshes, Road networks

## Slide 17: Static Results
Algorithm matches the oracle for 8/9 graphs
CU scaling less helpful
  Baseline already has 4 active CUs
  Matter of perspective

## Slide 18: Conclusions
Power optimizations depends heavily on graph structure
Frequency boosting is a useful technique
  Already implemented in contemporary HW
  We show that CU boosting is also useful
  …and that combining Frequency and CU boosting is even better
Simple graph metadata suffices for making power management decisions
  No preprocessing required
HW needs to support finer granularities of power management

## Slide 19: Questions
We would like to thank the NSF and AMD for their support

## Slide 20: Improvements: Dynamic Algorithm
Choose the best configuration at each iteration of the search
  Exhaustively test all iterations at all power configurations
  Choose the fastest of the ones that do not exceed the power cap
  Refer to this setting as the Dynamic Oracle
Two ways to improve over the static algorithm
  If the static algorithm classifies a graph incorrectly
  If the vertex frontiers change significantly in size
    Scale CUs when frontiers are small
    Scale frequency when frontiers are large

## Slide 21: Dynamic Results
Modest improvements
  ~5% overall
More variation in structure than available power states
  Need finer-grained methods of power management
Small number of iterations dominate
  Static case can optimize for these iterations