## Slide 1: Adaptive GPU Cache Bypassing
Yingying Tian* , Sooraj Puthoor†, Joseph L. Greathouse†, Bradford M. Beckmann†, Daniel A. Jiménez*
Texas A&M University*, AMD Research†

## Slide 2: Outline
Background and Motivation
Adaptive GPU Cache bypassing
Methodology
Evaluation Results
Case Study of Programmability
Conclusion

## Slide 3: Graphics Processing Units (GPUs)
Tremendous throughput
High performance computing
Target for general-purpose GPU computing
  Programming model: CUDA, OpenCL
  Hardware support: cache hierarchies
  AMD GCN: 16KB L1, NVIDIA Fermi: 16KB/48KB configurable
Notes: Graphics Processing Units provide tremendous throughput and high performance computing. GPUs have been designed for general purpose computing these years.
To better target for GPGPU workloads, programming models such as CUDA and openCL have been developed for easier programming. Hardware support such as cache hierarchies have been implemented in GPUs.
To achieve high performance and low overhead GPGPU computing with high programmability.
early GPUs focused on graphics applications that pose relatively fewer opportunities of data reuse. Specialized processor
GPGPU computing in the context of APU often involve diverse memory accessing patterns.
GCN, the architecture for future programmable and heterogeneous systems.

## Slide 4: Inefficiency of GPU Caches
  Thousands of concurrent threads
  Low per-thread cache capacity
Characteristics of GPU workloads
  Large data structures
  Useless insertion consumes energy
  Reducing the performance by replacing useful blocks
Scratchpad memories filter temporal locality
  Less reuse caught in caches
  Limit programmability
Notes: GPU caches are inefficient. The fact that thousands of concurrent threads are running at the same time in a gpu core, leads to very low per-thread cache capacity, plus the fact that gpu caches are usually smaller than cpu caches.
Another reason that leads to inefficient GPU caches is the the characteristics of GPU workloads.
They usually access large data structures that don’t fit in any reasonable cache sizes. Placing these data into caches consumes energy without any performance. Moreover, it trashes the cache by replacing useful blocks.

## Slide 5: Memory Characteristics
Zero-reuse blocks: inserted into caches without being accessed again until evicted
46% (max. 84%) of L1 cache blocks are only accessed once before eviction
Consume energy; pollute cache; cause more replacement
Chart: Dynamically Accessed Cache Blocks
| spmv | srad | bfs | lud | matrixmul | kmeans | histogram | backprop | nn | bitonic | dct | sort | nw | arith. mean
zero-reuse | 0.83934 | 0.82951 | 0.73934 | 0.65902 | 0.63934 | 0.58852 | 0.58197 | 0.39836 | 0.31803 | 0.21803 | 0.19836 | 0.027869 | 0.018033 | 0.46583
Notes: This figure shows the memory characteristics of GPGPU workloads in L1 caches. We defined two group of blocks. Zero-reuse, are blocks that are inserted into caches without being accessed again until evicted
We can see an average there are 46% of l1 blocks are only accessed once before their eviction. Insertion of those blocks consumes energy, pollutes the cache without any performance. These blocks should be bypassed from caches.

## Slide 6: Motivation
GPU caches are inefficient
Increasing cache sizes is impractical
Inserting zero-reuse blocks wastes power without performance gain
Inserting zero-reuse blocks causes useful blocks being replaced to reduce performance
Objective: Bypass zero-reuse blocks

## Slide 7: Outline
Background and Motivation
Adaptive GPU Cache bypassing
Methodology
Evaluation Results
Case Study of Programmability
Conclusion

## Slide 8: Bypass Zero-Reuse Blocks
Static bypassing on resource limit [Jia et. al 2014]
  Degrade the performance
Dynamic bypassing
  Adaptively bypass zero-reuse blocks
  Make prediction on cache misses
  What information shall we use to make prediction?
    Memory addresses
    Memory instructions
Notes: There are different ways to bypass zero-reuse blocks. Previous work proposed to do static bypassing when there is lack of resources. Static bypassing cannot differentiate useful blocks from zero reuse blocks, blindly bypassing may degrade the performance.
Another method is dynamic bypassing. It adaptively bypass zero-reuse blocks by making predictions on each cache miss. To make dynamic prediction, information such as memory addresses or memory instructions or both can be used.

## Slide 9: Memory Address vs. PC
Chart: Distinct Cache Blocks Accessed
| backprop | bfs | bitonic | dct | histogram | kmeans | lud | matrixmul | nn | nw | sort | spmv | srad | geomean
 | 49190.2834 | 695951.417 | 38259.1093 | 805263.1579 | 149392.7126 | 165789.4737 | 160323.8866 | 138461.5385 | 174898.7854 | 362550.6073 | 548380.5668 | 98380.5668 | 446356.2753 | 201200.3365
Using memory addresses is impractical due to storage
Using memory instructions consumes far less overhead
PCs generalize the behaviors of SIMD with high accuracy
Chart: Distinct PCs with Load Instructions
| backprop | bfs | bitonic | dct | histogram | kmeans | lud | matrixmul | nn | nw | sort | spmv | srad | geomean
 | 9 | 7 | 2 | 3 | 6 | 3 | 21 | 108 | 2 | 27 | 8 | 6 | 15 | 8.054
Notes: How can the hardware decide whether a block is zero-reuse on a cache Miss？
We quantified the number of distinct memory blocks s and the number of memory access instructions that are executed of each GPGPU workload as in these two figures.
As shown in the left figure, there are hundreds of thousands of distinct memory blocks are accessed during a gpu workload execution.
By contrast, as shown in the right figure, there are only tens to a hundred of distinct memory instructions.
That’s because of the nature of GPU workload.
They have small and highly parallel kernels. Each instruction accesses multiple data. Therefore PC can generalize the behavior of GPU workloads with high accuracy.

## Slide 10: Adaptive GPU Cache Bypassing
PC-based dynamic Bypass Predictor
  Inspired by dead block prediction in CPU caches [Lai et. al 2001][Khan et. al 2010]
    If a PC leads to the last access to one block, then the same PC will lead to the last access to other blocks
  On cache misses, predict if it is zero-reuse
    - If yes, requested block will bypass the cache
  On cache hits, verify previous prediction and make new prediction
Notes: We propose GPU cache bypassing,
It is a PC-based bypass predictor in L1 cache.

## Slide 11: Structure of PC-based Bypass Predictor
L1 cache
Cache accesses (PC, addr)
hashedPC (7-bit)
Tag
LRU bits
Valid bit
metadata
4-bit counter
Prediction table
128 entries
Update
Predict
HashedPC: the hash value of the PC of the last instruction that accessed this block
Notes: The structure of PC-based bypass predictor is very simple.

## Slide 12: Example
L1 cache
val
Prediction table
(PC, addr)
Hash(PC)
Get prediction
Miss
? Val >= threshold
block
CU
Bypass

## Slide 13: Example
L1 cache
val
Prediction table
(PC, addr)
Verify prediction
Hit
val = val -1
HashedPC
hashedPC = hash(PC)

## Slide 14: Example
L1 cache
val
Prediction table
Verify prediction
replacement
val = val +1
HashedPC

## Slide 15: Misprediction Correction
Bypass misprediction is irreversible
Cause additional penalties to access lower level caches
Utilize this procedure to help verify misprediction
Each L2 entry contains an extra bit: BypassBit
  BypassBit == 1 if the requested block will bypass L1
  Intuition: if it is a bypass misprediction, this block should be re-referenced soon, and will be hit in the L2 cache
Miscellaneous
  Set dueling
  Sampling

## Slide 16: Outline
Background and Motivation
Adaptive GPU Cache bypassing
Methodology
Evaluation Results
Case Study of Programmability
Conclusion

## Slide 17: Methodology
GPU cache configuration | 
CUs | 8, 1GHz, 64 scalar units by 4 SIMDs
L1 cache | 8-way, 16KB, 1-cycle tag, 4-cycle data access
Shared L2 cache | 16-way, 256KB, 4-cycle tag, 16-cycle data access
Shared L3 cache | 16-way, 4MB, 15-cycle tag, 30-cycle data access
In-house APU simulator that extends Gem5
  - Similar to AMD Graphics Core Next architecture
Benchmarks: Rodinia, AMD APP SDK, OpenDwarfs
Notes: We use oldest-first wavefront scheduling technique, which already minimize cache thrashing caused by round-robin
Our technique is orthogonal to cache-aware wavefront/warp scheduling techniques and can be used together for better performance.

## Slide 18: Storage Overhead
Evaluated Techniques
PC-based bypass predictor | 
Prediction table/L1 cache | 4-bit * 128 entries
Metadata/L1 block | 7 bits
Metadata/L2 block | 1 bit
Total cost | 224 bytes out of 16KB L1 (1.5%) 0.5KB out of 256KB L2 (0.2%)
Counter-based bypass predictor | 
Prediction table/L1 cache | 128* 128 entries, 5-bits
Metadata/L1 block | 20 bits (hashedPC, counters, prediction)
Total cost | 10.625KB out of 16KB L1 (66.4%)
Notes: Counters of events such as memory access intervals or number of references to make bypass prediction
Counter-based bypass prediction [27] is a CPU LLC by- passing technique. That work proposed to use an event counter in each cache block to record an event of interest such as cache accesses. When the counter reaches a thresh- old, the block observes no more reuse. This information is stored in a prediction table indexed by hashed block ad- dresses and PCs.

## Slide 19: Outline
Background and Motivation
Adaptive GPU Cache bypassing
Methodology
Evaluation Results
Case Study of Programmability
Conclusion

## Slide 20: Energy Savings
Chart: Percentage of Cache Misses Bypassed
| backprop | bfs | bitonic | dct | histogram | kmeans | lud | matrixmul | nn | nw | sort | spmv | srad | geomean
 | 0.34783 | 0.64251 | 0.66667 | 0.5 | 0.69807 | 0.81159 | 0.58696 | 0.72222 | 0.24879 | 0.96981 | 0.42029 | 0.71014 | 0.69324 | 0.58272
Chart: L1D Energy Usage vs. 16KB Cache
| backprop | bfs | bitonic | dct | histogram | kmeans | lud | matrixmul | nn | nw | sort | spmv | srad | geomean
 | 0.86 | 0.692 | 0.796 | 0.912 | 0.716 | 0.672 | 0.734 | 0.676 | 0.996 | 0.518 | 0.99 | 0.654 | 0.664 | 0.74783
58% of cache fills are prevented with cache bypassing
The energy cost of L1 cache is reduced by up to 49%, on average by 25%
Reduces dynamic power by 18% , increases the leakage power by only 2.5%
Notes: These two figures show the evaluation related to energy saving.
The left figure shoes the percentage of bypassed cache misses, on average there are 58% of cache fills are prevented with cache bypassing.
It leads to the energy cost reduction, as shown in the right figure, on average 25% of energy cost are reduced compared to the baseline.

## Slide 21: Performance Improvement
Chart: Performance Normalized to 16KB L1D
| backprop | bfs | bitonic | dct | histogram | kmeans | lud | matrixmul | nn | nw | sort | spmv | srad | geomean
32KB Cache | 1.0782 | 1.1153 | 0.97645 | 0.98558 | 0.99838 | 1.0124 | 1.0386 | 1.0532 | 1.0642 | 1.0008 | 1.0227 | 1.0203 | 1.0453 | 1.031
PC-based | 1.0435 | 1.1318 | 0.99838 | 0.99959 | 1.0032 | 0.99959 | 1.0197 | 1.0605 | 1.0081 | 1.0014 | 1.0282 | 1.0837 | 1.0404 | 1.0315
Counter-based | 0.99289 | 1.0234 | 1.0057 | 0.99594 | 1.0051 | 1.0057 | 1.0282 | 1.0891 | 1.0148 | 1.0002 | 1.0337 | 1.016 | 1.0526 | 1.0199
Outperforms counter-based predictor
Achieves performance of 32KB upper-bound
Notes: Besides reducing energy consumption, PC-based bypass predictor improves performance as well. As shown in this figure, PC-based bypass predictor outperforms counter-based predictor, and achieves similar performance of a double-sized L1 cache.
Different benchmarks have different characteristics. And therefore observe different performance improvement.
For example, benchmarks bfs, matrix multiply and spmv observes significant performance. That’s bc these benchmarks have relatively low L1 hit rate and very high reuse rate, thus, which cache bypassing, cache pollution victims are kept in caches for reuse.
Benchmark nw observes very little performance gain with bypassing. The reason is that nw puts all reused data into scratchpad memory for computation. Therefore there is very little reuse observed in caches. However, since most blocks are zero-reuse, with cache passing, 95% of cache blocks are bypassed to save energy.
We give detailed analysis of each benchmark in the paper.
------------------------------
significant performance improvement in benchmarks matrixmul, bfs, and spmv: these benchmarks observe intermediate or low L1 hit rate and very high reuse rate, so cache pollution victims
backprop and srad have intermediate to low L1 hit rate as well as a low reuse rate. So medium performance.
Benchmarks sort, dct, and lud are compute-bound benchmarks [10]. Increasing cache size does not significantly improve performance for these benchmarks. Energy is reduced.
Benchmarks kmeans and histogram invoke many kernel launches and frequently shared data between the CPU and the GPU. The performance is thus dominated by pulling data from CPU side,
enchmark bitonic contains frequent barrier synchronizations [17], causing the program to execute in lock-step with no observed performance improvement with any techniques while larger cache sizes degrade the performance due to the cache walk required when kernels complete.
nw puts all reused data into the scratchpad memory for computation and write through data to global memory when the computation is finished. with PC- based bypassing, benchmark nw has more than 95% of cache insertions prevented.

## Slide 22: Prediction Accuracy
Chart: Percent of L1D Accesses
| backprop | bfs | bitonic | dct | histogram | kmeans | lud | matrixmul | nn | nw | sort | spmv | srad | arith. mean | geo. mean
false positives | 0.2 | 0.06747 | 0.13735 | 0.2506 | 0.20964 | 0.14699 | 0.048193 | 0.089157 | 0.13735 | 0.057831 | 0.079518 | 0.048193 | 0.06747 | 0.11844 | 0.10181
coverage | 0.3494 | 0.64337 | 0.66988 | 0.50361 | 0.7012 | 0.81205 | 0.59036 | 0.72289 | 0.2506 | 0.97349 | 0.4241 | 0.71325 | 0.69639 | 0.61928 | 0.58535
False positives: incorrectly bypassed to-be-reused blocks
Coverage: the ratio of bypass prediction to all prediction
Coverage ratio is 58.6%, false positive rate is 12%
Notes: *false positive = #of access to predicted bypass blocks/ # of bypass predictions
*false positive is 1% for GPU cache bypassing

## Slide 23: Outline
Background and Motivation
Adaptive GPU Cache bypassing
Methodology
Evaluation Results
Case Study of Programmability
Conclusion

## Slide 24: Scratchpad Memories vs.Caches
Store reused data shared within a compute unit
Programmer-managed vs. hardware-controlled
Scratchpad memories filter out temporal locality
Limited programmability
  Explicitly remapping from memory address space to the scratchpad address space
To what extent can L1 cache bypassing make up for the performance loss caused by removing scratchpad memories?

## Slide 25: Case Study: Needleman-Wunsch (nw)
nw:
  Global optimization algorithm
  Compute-sensitive
  Very little reuse observed in L1 caches
Rewrote nw to remove the use of scratchpad memories: nw-noSPM
  Not simply replace _local_ functions with _global_ functions
  Best-effort re-written version

## Slide 26: Case Study (cont.)
Chart: Kernel Execution Time (milliseconds)
| nw-16KB | nw-32KB | nw-64KB | nw-Bypass | nw-128KB | nw-256KB | nw_noSPM-16KB | nw_noSPM-32KB | nw_noSPM-64KB | nw_noSPM-Bypass-16KB | nw_noSPM-128KB | nw_noSPM-256KB
 | 25.3061 | 25.3061 | 25.3061 | 25.3061 | 25.3061 | 25.3061 | 178.7755 | 171.8367 | 157.9592 | 124.4898 | 80.8163 | 63.6735
Nw-noSPM takes 7X longer than nw
With bypassing, the gap is reduced by 30%
16KB L1 cache + bypassing outperforms 64KB L1 cache
Note that scratchpad memory is 64KB while L1 is only 16KB
Notes: This limited study shows that, while the technique currently cannot replace scratchpad memories programmed by expert programmers, it can reduce the performance gap when such programming effort is impractical.

## Slide 27: Conclusion
GPU caches are inefficient
We propose a simple but effective GPU cache bypassing technique
Improves GPU cache efficiency
Reduces energy overhead
Requires far less storage overhead
Bypassing allows us to move towards more programmable GPUs

## Slide 28
Thank you!
Questions?

## Slide 29: Backup
Do all zero-reuse actually streaming?
Chart: Dynamically Accessed Cache Blocks
| spmv | srad | bfs | lud | matrixmul | kmeans | histogram | backprop | nn | bitonic | dct | sort | nw | arith. mean
lifeLongNoReuse | 0.016393 | 0.54918 | 0.0016393 | 0 | 0 | 0 | 0.57869 | 0.21803 | 0 | 0 | 0.19836 | 0.029508 | 0 | 0.12245
zero-reuse | 0.83934 | 0.82951 | 0.73934 | 0.65902 | 0.63934 | 0.58852 | 0.58197 | 0.39836 | 0.31803 | 0.21803 | 0.19836 | 0.027869 | 0.018033 | 0.46583
Notes: Lifelongnoreuse: blocks that are only accessed once during the execution of the whole program.
In other words, the blue bar shows the lifelongdead blocks while the red bar shows dead blocks due to conflict misses.

## Slide 30: GPU Cache Capacity
Chart: sizes of L1 cache
| 32KB | 64KB | 128KB | 256KB | 512KB | 1024KB
 | 1.04 | 1.12 | 1.36 | 1.382 | 1.44 | 1.475
Caches are useful, but current cache size are too small to gain benefit
Performance benefit by increasing cache sizes << extra area taken up
Adding more computational resources
Leading to lower per-thread cache capacity
Notes: TODO: explain more. Doesn’t show what the problem is.

## Slide 31: Power Overhead
Energy (nJ) | 16KB baseline | bypassing
per tag access | 0.00134096 | 0.0017867
per data access | 0.106434 | 0.106434
per prediction table access | N/A | 0.000126232
Dynamic Power (mW) | 44.2935 | 36.1491
Static Power (mW) | 7.538627 | 7.72904

## Slide 32: Compare with SDBP
SDBP is designed for LLCs, where much of the temporal locality has been filtered
our technique is designed for GPU L1 caches, where temporal information is complete. We use PCs because of the observation of characteristics of GPGPU memory accesses.
GPU kernels are small and frequently launched, the interleaving changes frequently.