## Slide 1: Dynamic GPGPU Power Management Using Adaptive Model Predictive Control
Abhinandan Majumdar*, Leonardo Piga†, Indrani Paul†,
Joseph L. Greathouse†, Wei Huang†, David H. Albonesi*
*Computer Systems Laboratory, Cornell University
†Advanced Micro Devices, Inc.

## Slide 2: Model Predictive Control (MPC)
Previous dynamic power management policies ignore future application behavior
  Leads to performance loss or wasted energy
MPC looks into the future to determine the best configuration for the current optimization time step
Though effective in many domains, overheads far too high for short timescales of dynamic power management
Our approach: An approximation of MPC that dramatically improves GPGPU energy-efficiency with orders of magnitude lower overhead
Notes: With Model Predictive Control we look ahead into the future in order to determine the best configuration for the current timestep. MPC has been shown to be highly effective in many problem domains, but it’s overhead is far too high for online dynamic power management. We’ve developed an approximation of MPC that achieves significant gains in GPGPU energy-efficiency with orders of magnitude lower overhead.

## Slide 3: Dynamic GPGPU Power Management
Attempts to maximize performance within power constraints
Hardware knobs
  Number of active GPU Compute Units
  DVFS states
Goal: Reduce the energy of the GPU application phases compared to the baseline power manager while matching its performance

## Slide 4: Applying MPC to Dynamic Power Management
General Idea
MPC has high overhead
  Complexity scales exponentially with H
  Minimizing energy under performance cap with discrete HW settings is fundamentally NP-hard
  Usually requires dedicated optimization solvers, such as CVX, lpsolve, etc.
Horizon H
Apply here
GPU kernels

## Slide 5: Approximations to MPC
Greedy Hill Climbing to reduce the search space
Static search order heuristic to make MPC optimization polynomial rather than exponential
Dynamically tuning of the horizon length H to limit the optimization overhead

## Slide 6: MPC Power Manager Architecture
Kernel
HW setting
Performance
Power Model
Performance Tracker
Performance
Feedback
MPC Optimizer
Optimizer
Performance
Power
Perf. Counters of
Future
Kernels
Kernel Pattern Extractor
Performance
Counters
Performance
Target
Adaptive Horizon Generator
Horizon Length
Optimization Overhead
Max Overhead

## Slide 7: MPC Optimizer
Greedy Hill Climbing optimization
  Select the HW knob with highest energy sensitivity
  Search for the lowest energy configuration using hill climbing
MPC Search Heuristic
  Determines a static order without backtracking
  Search cost becomes polynomial
  Details in the paper
65X average reduction in total cost evaluations
Objective: Find minimum energy HW setting for each kernel without impacting overall performance

## Slide 8: Adaptive Horizon Generator
Limit the overhead to a slowdown factor by dynamically varying the horizon length
General Idea:
Longer horizon improves savings but increases MPC optimization time
Est. MPC Overhead + Perf. Loss
Increase
Horizon Length
Decrease
Horizon Length
Yes
No

## Slide 9: MPC in Action – An Example
Time
Past
Past
Performance
Future Execution Pattern
Setting for kernel 1 applied
Perf. Tracker
MPC
Optimizer
Optimizer
Search order
(2, 1, 4, 5, 3, 6)
2
1
A
B
A

## Slide 10: MPC in Action – An Example
Time
Past
Updated
Past
Performance
Updated
Future Execution Pattern
Setting for kernel 2 applied
Search order
(2, 1, 4, 5, 3, 6)
2
C
A
C
A
A
Optimizer
Perf. Tracker
MPC
Optimizer

## Slide 11: Experimental Testbed
AMD A10-7850K APU
  2 out-of-order dual core CPUs
  GPU contains 512 processing elements (8 CUs) at 720 MHz
DVFS states
Total HW configuration: 336
NB and GPU share the same voltage rail
CPU P States | Voltage (V) | Freq (GHz)
P1 | 1.325 | 3.9
P2 | 1.3125 | 3.8
P3 | 1.2625 | 3.7
P4 | 1.225 | 3.5
P5 | 1.0625 | 3
P6 | 0.975 | 2.4
P7 | 0.8875 | 1.7
NB P States | Freq (GHz) | Memory Freq (MHz)
NB0 | 1.8 | 800
NB1 | 1.6 | 800
NB2 | 1.4 | 800
NB3 | 1.1 | 333
GPU P States | Voltage (V) | Freq (GHz)
DPM0 | 0.95 | 351
DPM1 | 1.05 | 450
DPM2 | 1.125 | 553
DPM3 | 1.1875 | 654
DPM4 | 1.225 | 720

## Slide 12: Experimental Setup
15 GPGPU Benchmarks
Baseline scheme
  AMD Turbo Core
Predict Previous Kernel (PPK)
  Assume last kernel repeats
  State-of-the-art: Harmonia ISCA’15, McLaughlin et al. ASBD’14
Maximum overhead = 5%
Category | Benchmarks | Benchmark Suite | Regular Expression
Regular | mandelbulbGPU | Phoronix | A20
 | Nbody | AMD APP SDK | A10
 | juliaGPU | Phoronix | A10
Irregular with repetitive pattern | EigenValue | AMD APP SDK | (AB)5
 | XSBench | Exascale | (ABC)2
Irregular with non-repetitive pattern | Spmv | SHOC | A10B10C10
 | Kmeans | Rodinia | AB20
Irregular with kernels varying with input | swat | OpenDwarfs | Complex pattern
 | color | Pannotia | 
 | pb-bfs | Parboil | 
 | mis | Pannotia | 
 | srad | Rodinia | 
 | lulesh | Exascale | 
 | lud | Rodinia | 
 | hybridsort | Rodinia | 

## Slide 13: Energy-Performance Gains
Chart: Relative Performance
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Irregular-all | Irregular-var-input | Average
Predict Previous Kernel | 1.0031 | 1 | 1.0431 | 0.918 | 0.83245 | 0.80675 | 0.98865 | 0.92455 | 0.87582 | 0.97375 | 0.93604 | 0.73503 | 0.83454 | 0.91911 | 0.75297 | 0.8748 | 0.86898 | 0.90292
MPC_ALL | 0.99874 | 0.99976 | 1.0395 | 0.97599 | 0.98514 | 0.96968 | 0.99811 | 0.98459 | 0.99817 | 0.98292 | 0.99394 | 0.8436 | 0.98757 | 1.0172 | 0.96235 | 0.97494 | 0.97129 | 0.98248
Chart: Energy Savings (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Irregular-all | Irregular-var-input | Average
Predict Previous Kernel | 27.4553 | 8.0026 | 47.1442 | 4.6334 | 9.107 | 13.5398 | 28.5204 | 14.2334 | 14.3635 | 31.1604 | 15.8879 | 8.5721 | 16.987 | 26.3413 | 27.1571 | 17.5419 | 19.3378 | 19.5404
MPC | 27.2007 | 7.9908 | 51.7434 | 6.1279 | 7.1307 | 24.1886 | 28.9585 | 17.6415 | 23.5476 | 31.5879 | 19.2602 | 24.8987 | 28.0892 | 33.6115 | 39.7433 | 23.7321 | 27.2975 | 24.7814
24.8%
-1.8%
-10%
19.5%

## Slide 14: MPC Overhead
Chart: MPC Energy Overhead (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Average
MPC_ALL | 0.2653 | 0.016212 | 0.038328 | 0.0012385 | 0.0021781 | 0.52902 | 0.12678 | 0.097247 | 0.035248 | 0.041775 | 0.060636 | 0.1352 | 0.08408 | 0.35053 | 0.51355 | 0.15316
Chart: MPC Performance Overhead (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Average
MPC_ALL | 0.60145 | 0.033477 | 0.091724 | 0.002463 | 0.0043155 | 1.1815 | 0.31501 | 0.20564 | 0.075449 | 0.087714 | 0.11877 | 0.31913 | 0.19813 | 0.83289 | 0.81394 | 0.32544
0.2%
0.3%
Chart: % Avg. Horizon Length
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort
MPC_ALL | 90.5 | 100 | 100 | 100 | 100 | 8.3333 | 57.8231 | 88.8889 | 0.33333 | 0 | 1.385 | 76.5432 | 0.17796 | 0.073326 | 7.5556

## Slide 15: Ramification of Prediction Inaccuracy
RF: 12% Power, 25% Perf
15% Power, 10% Perf: Wu et al. [HPCA 2015]
5% Power, 5% Perf: Paul et al. [ISCA 2015]
Chart: Relative Performance
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Average
RF | 1.0048 | 1.0001 | 1.0404 | 0.97602 | 0.98518 | 0.98149 | 1.0013 | 0.98665 | 0.99893 | 0.9838 | 0.99513 | 0.84679 | 0.98955 | 1.0255 | 0.97048 | 0.98317
Err_15%_10% | 0.97506 | 0.99833 | 1.2638 | 0.97614 | 0.98782 | 0.99014 | 1.0165 | 0.97612 | 0.99388 | 0.9838 | 0.99513 | 1.0083 | 0.98955 | 1.0255 | 1.0736 | 1.0216
Err_5% | 0.98865 | 0.99885 | 1.2624 | 0.99935 | 0.9901 | 0.98818 | 1.0154 | 0.99592 | 0.99893 | 0.9838 | 0.99513 | 1.0083 | 0.98955 | 1.0255 | 1.1232 | 1.0289
Err_0% | 1.0133 | 1.0001 | 1.1934 | 1.0001 | 0.97159 | 0.99147 | 1.0018 | 1.0018 | 0.9987 | 0.9838 | 0.99513 | 0.98308 | 0.98955 | 1.0255 | 1.0815 | 1.0167
Chart: Energy Savings (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Average
RF | 27.466 | 8.007 | 51.7817 | 6.1291 | 7.1329 | 24.7177 | 29.0853 | 17.7388 | 23.5829 | 31.6297 | 19.3208 | 25.0339 | 28.1733 | 33.962 | 40.2568 | 24.9345
15% Power, 10% Perf | 26.2565 | 7.9643 | 53.5252 | 6.039 | 5.8097 | 25.0191 | 37.1521 | 23.9142 | 27.4573 | 31.6297 | 19.3208 | 34.0295 | 28.1733 | 33.962 | 47.2694 | 27.1681
5% Power, 5% Perf | 27.5364 | 7.8139 | 58.7132 | 6.8826 | 5.8832 | 24.9424 | 39.251 | 18.0843 | 23.5829 | 31.6297 | 19.3208 | 33.9761 | 28.1733 | 33.962 | 51.777 | 27.4352
Perfect | 28.4813 | 8.0071 | 57.0118 | 6.7326 | 7.5346 | 25.038 | 31.6841 | 18.5075 | 34.2175 | 31.6297 | 19.3208 | 34.7773 | 28.1733 | 33.962 | 53.3137 | 27.8927

## Slide 16: Conclusions
MPC looks into the future to determine the best configuration for the current optimization time step
Though effective in many domains, overheads far too high for short timescales of dynamic power management
We devise an approximation of MPC that dramatically improves GPGPU energy-efficiency with orders of magnitude lower overhead
Our approach reduces energy by 24.8% with only a 1.8% performance impact

## Slide 17: Questions

## Slide 18: Backup Slides

## Slide 19: Performance-aware Power Management
Optimum node-level power efficiency is a complex function of SOC configuration, workload characteristics, programming model, and node-level objective/constraints
Performance
Knob 1
High Perf/Watt
Knob 2
Low Perf/Watt
HW Knobs: DVFS states of CPU, GPU, NB etc.
Watt
User Application
Host Tasks
GPU Tasks
Programming Model
Time-varying Workload
Reduce energy of the GPGPU kernel phase while performing better than a target
Non-linear power vs. performance curves
Maximize Perf under Power/Thermal cap
Minimize Power under Perf cap

## Slide 20: Model Predictive Control (MPC)
MPC looks into the future to determine the best configuration for the current optimization time step
Though effective in many domains, overheads far too high for short timescales of dynamic power management
Our approach: An approximation of MPC that dramatically improves GPGPU energy-efficiency with orders of magnitude lower overhead
Horizon H
Current timestep
Shift horizon
Notes: With Model Predictive Control we look ahead into the future in order to determine the best configuration for the current timestep. MPC has been shown to be highly effective in many problem domains, but it’s overhead is far too high for online dynamic power management. We’ve developed an approximation of MPC that achieves significant gains in GPGPU energy-efficiency with orders of magnitude lower overhead.

## Slide 21: Dynamic GPGPU Power Management
CPU and GPU consume significant power in servers
Previous approaches to dynamic power management are locally predictive and ignore future kernel behavior
  Performance loss or wasted energy
Applying MPC is challenging for short timescales of dynamic power management
Goal: Approximations to MPC that save GPGPU energy within the timescales of a typical server operation without degrading performance
Model Predictive Control
Proactively looks ahead into the future

## Slide 22: Dynamic GPGPU Power Management
Goal: Reduce GPGPU energy within the timescales of a typical server operation without degrading performance
Computationally Intensive
  NP-Hard
  Challenging for short timescales of dynamic power management
Idea: Improve energy efficiency by looking into future phases
  Model Predictive Control (MPC)
  Dynamically vary computation to limit performance overhead

## Slide 23: Traditional Energy Management
Static
  Predefined set of decisions
Reactive
  Act after sensing a change in behavior
Locally Predictive
  Predict the immediate behavior
Performance loss or wasted energy
Proactive Energy Management
Adapt from past and look-ahead into the future

## Slide 24: Motivating Future Awareness
Baseline
  AMD Turbo Core
Hardware Knobs
  DVFS states, GPU CUs
Predict Previous Kernel (PPK):
  Assume last kernel repeats
  State-of-the-art: Harmonia ISCA’15, McLaughlin et al. ASBD’14
Theoretically Optimal (TO):
  Perfect knowledge of future
  Impractical
Chart: Energy Savings (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort
Predict Previous Kernel | 26.6176 | 7.9578 | 63.002 | -1.1008 | 0.9858 | 24.8162 | 30.9711 | 18.4116 | 22.1736 | 32.4452 | 22.5084 | -10.1516 | -5.0999 | 27.3065 | 40.0278
Theoretically Optimal | 28.7401 | 8.0071 | 63.3627 | 6.7597 | 22.6278 | 29.8781 | 46.9156 | 25.2726 | 40.7754 | 53.3993 | 39.0427 | 39.3485 | 43.3182 | 45.0672 | 57.3401
Chart: Speedup
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort
Predict Previous Kernel | 1.0034 | 0.99961 | 1.4418 | 0.87866 | 0.81135 | 0.96294 | 1.0025 | 0.99744 | 0.9644 | 0.96238 | 0.99205 | 0.57563 | 0.55469 | 0.91468 | 0.94536
Theoretically Optimal | 1.0189 | 1.0001 | 1.4544 | 1 | 1.0118 | 1 | 1.0316 | 1 | 1 | 1.0561 | 1.0007 | 1.0159 | 1.0123 | 1 | 1.1486
50%
46%

## Slide 25: Ramifications of Ignoring Future
Spmv
Performance
Loss
Chart: Kernel Execution Order
Baseline | 1.5868 | 1.5669 | 1.5803 | 1.5812 | 1.5709 | 1.5665 | 1.5595 | 1.5662 | 1.5808 | 1.5781 | 0.98374 | 0.97424 | 0.97352 | 0.97423 | 0.98014 | 0.97161 | 0.97923 | 0.97902 | 0.97414 | 0.97077 | 0.3666 | 0.36509 | 0.36464 | 0.36423 | 0.36505 | 0.3644 | 0.36123 | 0.36395 | 0.3639 | 0.36498
PPK | 1.5765 | 1.5737 | 1.569 | 1.5718 | 1.5698 | 1.5732 | 1.2695 | 1.4547 | 1.5705 | 1.2706 | 0.78174 | 0.95907 | 0.97173 | 0.95983 | 0.96938 | 0.95978 | 0.96017 | 0.96328 | 0.96853 | 0.95672 | 0.36122 | 0.36289 | 0.36402 | 0.35501 | 0.35265 | 0.36234 | 0.3312 | 0.36668 | 0.36166 | 0.36141
Target | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Kernel Execution Order
Baseline | 1.5868 | 1.5768 | 1.5779 | 1.5788 | 1.5772 | 1.5754 | 1.5731 | 1.5722 | 1.5732 | 1.5737 | 1.535 | 1.5002 | 1.4694 | 1.4421 | 1.4181 | 1.3958 | 1.3762 | 1.3583 | 1.3417 | 1.3262 | 1.2797 | 1.2371 | 1.1984 | 1.1628 | 1.1303 | 1.1002 | 1.072 | 1.0462 | 1.0223 | 1
PPK | 1.5765 | 1.5751 | 1.5731 | 1.5728 | 1.5722 | 1.5724 | 1.5205 | 1.512 | 1.5183 | 1.4892 | 1.4347 | 1.4066 | 1.3826 | 1.3603 | 1.3409 | 1.3226 | 1.3061 | 1.2912 | 1.2778 | 1.2649 | 1.2224 | 1.1839 | 1.1489 | 1.1156 | 1.0847 | 1.0573 | 1.0283 | 1.0053 | 0.98343 | 0.96294
Target | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PPK lowers performance
Avoid performance slowdown
Look ahead

## Slide 26: Ramifications of Ignoring Future
Kmeans
Chart: Kernel Execution Order
Kernel Performance | 0.095251 | 1.0779 | 1.078 | 1.0781 | 1.0777 | 1.078 | 1.0776 | 1.0774 | 1.0756 | 1.0779 | 1.0777 | 1.0778 | 1.0777 | 1.0773 | 1.0778 | 1.0755 | 1.078 | 1.078 | 1.078 | 1.078 | 1.078
Runtime Speedup | 0.095251 | 0.45706 | 0.62415 | 0.7204 | 0.78292 | 0.82686 | 0.85936 | 0.88439 | 0.90411 | 0.92033 | 0.93376 | 0.94508 | 0.95475 | 0.96308 | 0.97038 | 0.97668 | 0.98239 | 0.9875 | 0.99209 | 0.99624 | 1
Target | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Kernel Execution Order
PPK | 33.5868 | 30.4524 | 30.5396 | 30.5876 | 30.4837 | 29.8788 | 29.79 | 29.9407 | 29.9496 | 30.1309 | 30.2273 | 30.2385 | 30.1775 | 30.1759 | 30.0901 | 30.1755 | 30.241 | 30.293 | 30.2175 | 30.2173 | 30.9711
TO | 65.4807 | 55.9718 | 52.6835 | 51.0339 | 49.9281 | 48.6453 | 48.1409 | 48.0393 | 47.8255 | 47.7466 | 47.5708 | 47.4678 | 47.3051 | 47.2609 | 47.1047 | 47.0947 | 47.0837 | 47.0915 | 46.9874 | 46.9624 | 46.9156
PPK spends lot of energy
Look ahead
Catch up on performance

## Slide 27: Background
Typical GPGPU application phase
…
CPU
DATA
TRANSFER
GPU Kernel
CPU
DATA
TRANSFER
CPU
DATA
TRANSFER
GPU Kernel
CPU
DATA
TRANSFER
CPU
Time

## Slide 28: Kernel Performance Scaling
Energy-optimal configuration differ across kernels

## Slide 29: Model Predictive Control (MPC)
General Idea
MPC Components
  Accurate system model
  Future input forecast
  Optimization
Horizon H
Apply here
  Power and performance prediction model
  Kernel pattern extractor
  Greedy and heuristic based optimizer

## Slide 30: Feedback-based Performance Tracker
Performance met previously?
Optimize Aggressively
Reduce energy
Avoid performance loss
Relax optimization
Spend energy
Reduce performance loss
Yes
No
Switch the optimization goal based on past performance and the target

## Slide 31: Performance Power Model
Kernel
HW setting
Performance
Power Model
Performance Tracker
Performance
Feedback
MPC Optimizer
Optimizer
Performance
Power
Perf. Counters of
Future
Kernels
Kernel Pattern Extractor
Performance
Counters
Performance
Target
Adaptive Horizon Generator
Horizon Length
Optimization Overhead
Max Overhead
Trained offline using Random Forest Learning Algorithm
Estimates performance and power for any HW configuration

## Slide 32: Kernel Pattern Extractor
Kernel
HW setting
Performance
Power Model
Performance Tracker
Performance
Feedback
MPC Optimizer
Optimizer
Performance
Power
Perf. Counters of
Future
Kernels
Kernel Pattern Extractor
Performance
Counters
Performance
Target
Adaptive Horizon Generator
Horizon Length
Optimization Overhead
Max Overhead
Extracts kernel execution pattern upon the first encounter
Stores the performance counters of dissimilar kernels and retunes it

## Slide 33: MPC Optimizer
Greedy Hill Climbing optimization
  Using the predictor, select the HW knob with highest energy sensitivity
  Search for low energy configuration using hill climbing
CPU DVFS
NB DVFS
GPU DVFS
GPU CU
Predicted Energy
GPU DVFS states
Hill climbing

## Slide 34: MPC Optimizer
Greedy Hill Climbing optimization
  Using the predictor, select the HW knob with highest energy sensitivity
  Search for low energy configuration using hill climbing
CPU DVFS
NB DVFS
GPU DVFS
GPU CU
Predicted Energy
GPU CU count
Hill climbing
20 cost reduction over exhaustive

## Slide 35: MPC Optimizer
Greedy Hill Climbing optimization
  Select the HW knob with highest energy sensitivity and search for low energy configuration using hill climbing
MPC Search Heuristic
  Determine a static order requiring no backtracking
  General Idea
    High to low performance (e.g. Spmv): Optimize low performing kernels first
    Low to high performance (e.g. Kmeans): Optimize high performing kernels first
  Search cost becomes polynomial
Chart: Kernel Execution Order
| K1 | K2 | K3 | K4 | K5 | K6
Kernel Throughput | 2.3134 | 1.6468 | 0.43509 | 0.23615 | 0.88782 | 2.9768
Runtime Throughput | 2.3134 | 1.7837 | 1.7029 | 0.88051 | 0.88096 | 1
(Low Performance)
Optimize Second
(High Performance)
Optimize First
65 reduction in cost evaluation
Performance
Performance
(3, 2, 1, 6, 5, 4)

## Slide 36: MPC Optimizer
MPC Search Heuristic
  Determine a static order requiring no backtracking
  General Idea
    High to low performance (e.g. Spmv): Optimize low performing kernels first
    Low to high performance (e.g. Kmeans): Optimize high performing kernels first
  Search cost becomes polynomial
Chart: Kernel Execution Order
| K1 | K2 | K3 | K4 | K5 | K6
Kernel Throughput | 2.3134 | 1.6468 | 0.43509 | 0.23615 | 0.88782 | 2.9768
Runtime Throughput | 2.3134 | 1.7837 | 1.7029 | 0.88051 | 0.88096 | 1
(Low Performance)
Optimize Second
(High Performance)
Optimize First
65 cost reduction
Performance
Performance
(3, 2, 1, 6, 5, 4)

## Slide 37: Adaptive Horizon Generator
MPC runs between kernel invocations
Longer horizon increases MPC optimization time
Limit the overhead by dynamically varying the horizon length
General Idea:
Kernels
MPC

## Slide 38: Dynamic GPGPU Power Mgmt. Formulation
Minimize energy over GPU kernels such that the performance target is met

## Slide 39: Theoretically Optimal
GLPK to solve the Integer Linear Programming (ILP) formulation

## Slide 40: Predict Previous Kernel (PPK)
Minimize energy of kernel such that the runtime performance so far exceeds the target

## Slide 41: MPC-based GPGPU Power Manager
Optimize energy for next kernels such that the runtime performance at the end of kernels exceeds the target

## Slide 42: Runtime Performance Tracker
Performance requirement of kernel, , is enforced as follows:
Kernel time headroom is updated according to:

## Slide 43: Feedback-based Performance Tracker
Performance met previously?
Optimize Aggressively
Reduce energy
Avoid performance loss
Relax optimization
Spend energy
Reduce performance loss
Yes
No

## Slide 44: MPC Optimizer
Greedy Hill Climbing optimization
  Select the HW knob with highest energy sensitivity and search for low energy configuration using hill climbing
MPC Search Heuristic
  Determine a static order requiring no backtracking
  General Idea
    High to low performance (e.g. Spmv): Optimize low performing kernels first
    Low to high performance (e.g. Kmeans): Optimize high performing kernels first
  Search cost becomes polynomial
65X average reduction in total cost evaluations
An Example
Search order = (2, 1, 4, 5, 3)
H
Apply here
2
1

## Slide 45: MPC Optimizer
Greedy hill climbing optimization
  Greedy: Select the HW knob with highest energy sensitivity
  Hill Climbing: Continue finding low energy configuration (within perf target), and stop
  Reduces search cost by 20X
MPC Search Heuristic
  Determine a static order requiring no backtracking
  General Idea
    High to low performance (e.g. Spmv): Optimize low performing kernels first
    Low to high performance (e.g. Kmeans): Optimize high performing kernels first
  Search becomes polynomial
Average reduction in total cost evaluations: 65X
An Example
Search order = (2, 1, 4, 5, 3)
2
H
Apply here

## Slide 46: GPGPU Benchmarks
Category | Benchmarks | Benchmark Suite | Regular Expression
Regular | mandelbulbGPU | Phoronix | A20
 | Nbody | AMD APP SDK | A10
 | juliaGPU | Phoronix | A10
Irregular with repetitive pattern | EigenValue | AMD APP SDK | (AB)5
 | XSBench | Exascale | (ABC)2
Irregular with non-repetitive pattern | Spmv | SHOC | A10B10C10
 | Kmeans | Rodinia | AB20
Irregular with kernels varying with input | swat | OpenDwarfs | Complex pattern
 | color | Pannotia | 
 | pb-bfs | Parboil | 
 | mis | Pannotia | 
 | srad | Rodinia | 
 | lulesh | Exascale | 
 | lud | Rodinia | 
 | hybridsort | Rodinia | 

## Slide 47: Experimental Testbed (Detailed)
AMD A10-7850K APU
  2 out-of-order dual core CPUs
  GPU contains 512 processing elements (8 CUs) at 720 MHz
    Each CU has 4 SIMD Vector Units
    16 PEs per SIMD vector unit
DVFS states
NB and GPU share the same voltage rail
CPU P States | Voltage (V) | Freq (GHz)
P1 | 1.325 | 3.9
P2 | 1.3125 | 3.8
P3 | 1.2625 | 3.7
P4 | 1.225 | 3.5
P5 | 1.0625 | 3
P6 | 0.975 | 2.4
P7 | 0.8875 | 1.7
NB P States | Freq (GHz) | Memory Freq (MHz)
NB0 | 1.8 | 800
NB1 | 1.6 | 800
NB2 | 1.4 | 800
NB3 | 1.1 | 333
GPU P States | Voltage (V) | Freq (GHz)
DPM0 | 0.95 | 351
DPM1 | 1.05 | 450
DPM2 | 1.125 | 553
DPM3 | 1.1875 | 654
DPM4 | 1.225 | 720
GPU CUs and DVFS states changed in multiples of 2
Total HW configuration: 336

## Slide 48: Experimental Setup
15 GPGPU Benchmarks
  Sampled from 73 benchmarks
  75% irregular
  44% vary with input
Baseline scheme
  AMD Turbo Core
Algorithms
  PPK
  MPC
  TO
Results based on real hardware traces
Category | Benchmarks | Benchmark Suite | Regular Expression
Regular | mandelbulbGPU | Phoronix | A20
 | Nbody | AMD APP SDK | A10
 | juliaGPU | Phoronix | A10
Irregular with repetitive pattern | EigenValue | AMD APP SDK | (AB)5
 | XSBench | Exascale | (ABC)2
Irregular with non-repetitive pattern | Spmv | SHOC | A10B10C10
 | Kmeans | Rodinia | AB20
Irregular with kernels varying with input | swat | OpenDwarfs | Complex pattern
 | color | Pannotia | 
 | pb-bfs | Parboil | 
 | mis | Pannotia | 
 | srad | Rodinia | 
 | lulesh | Exascale | 
 | lud | Rodinia | 
 | hybridsort | Rodinia | 

## Slide 49: Polynomial MPC w/ Theoretical Optimal
Chart: Energy Savings (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Irregular-all | Irregular-var-input | Average
MPC | 28.7401 | 8.0071 | 63.3627 | 6.9896 | 18.3064 | 26.4636 | 45.5138 | 22.614 | 38.8937 | 43.0561 | 30.6621 | 35.998 | 41.4531 | 39.2735 | 56.3474 | 33.7976 | 38.5372 | 33.7121
Theoretically Optimal | 28.7401 | 8.0071 | 63.3627 | 6.7597 | 22.6278 | 29.8781 | 46.9156 | 25.2726 | 40.7754 | 53.3993 | 39.0427 | 39.3485 | 43.3182 | 45.0672 | 57.3401 | 37.4788 | 42.9455 | 36.657
Chart: Speedup
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Irregular-all | Irregular-var-input | Average
MPC | 1.0189 | 1.0001 | 1.4544 | 0.99873 | 1.0109 | 0.98965 | 1.0329 | 1.0004 | 1.0022 | 1.0164 | 0.99486 | 1.0049 | 1.0146 | 1.0182 | 1.1386 | 1.0185 | 1.0238 | 1.0464
Theoretically Optimal | 1.0189 | 1.0001 | 1.4544 | 1 | 1.0118 | 1 | 1.0316 | 1 | 1 | 1.0561 | 1.0007 | 1.0159 | 1.0123 | 1 | 1.1486 | 1.0231 | 1.0292 | 1.05
92%
93%

## Slide 50: GPU Energy Savings
Chart: GPU Energy Savings (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Irregular-all | Irregular-var-input | Average
Predicted Previous Kernel | 7.5915 | 6.8086 | 41.2157 | 11.6997 | 26.0484 | 5.5039 | 4.5938 | 4.2279 | -8.6759 | -5.7836 | 1.1105 | -29.1324 | -6.4035 | -0.55621 | 3.3625 | 0.49959 | -5.2313 | 4.1074
MPC | 7.4543 | 6.8086 | 51.4691 | 9.8746 | 9.0789 | 11.8514 | 4.5938 | 4.5274 | 3.2114 | -5.7836 | 5.2339 | 4.2388 | 4.8904 | 8.0079 | 19.7451 | 6.6225 | 5.5089 | 9.6801

## Slide 51: MPC Energy-Performance w.r.t PPK
Chart: Energy Savings (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Irregular-all | Irregular-var-input | Average
MPC_ALL | -0.35091 | -0.012873 | 8.7014 | 1.5671 | -2.1743 | 12.3164 | 0.61295 | 3.9738 | 10.7245 | 0.62106 | 4.0093 | 17.8574 | 13.374 | 9.8701 | 17.2785 | 7.5026 | 9.7136 | 6.5579
Chart: Speedup
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Irregular-all | Irregular-var-input | Average
MPC_ALL | 0.99568 | 0.99976 | 0.99644 | 1.0632 | 1.1834 | 1.2026 | 1.0094 | 1.0671 | 1.1395 | 1.009 | 1.0603 | 1.1481 | 1.1822 | 1.1053 | 1.2725 | 1.1202 | 1.123 | 1.0956

## Slide 52: Amortization of Initial Loses
Chart: Energy Savings (%)
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Average
1 | -0.17546 | -0.0064231 | 4.2982 | 0.7851 | -1.0866 | 4.7406 | 0.29997 | 1.8776 | 3.4826 | 0.0073359 | 1.2964 | 8.2968 | 3.8146 | 1.3116 | 4.2512 | 2.2129
10 | -0.31901 | -0.011698 | 7.8928 | 1.4251 | -1.9764 | 10.6194 | 0.55504 | 3.5747 | 8.8783 | 0.06631 | 3.3155 | 16.0123 | 10.6941 | 5.9727 | 13.2256 | 5.3283
100 | -0.34744 | -0.012745 | 8.6131 | 1.5516 | -2.1527 | 12.1227 | 0.60662 | 3.9299 | 10.506 | 0.33816 | 3.9271 | 17.654 | 13.047 | 9.2655 | 16.7647 | 6.3876
Steady state | -0.35091 | -0.012873 | 8.7014 | 1.5671 | -2.1743 | 12.3164 | 0.61295 | 3.9738 | 10.7245 | 0.62106 | 4.0093 | 17.8574 | 13.374 | 9.8701 | 17.2785 | 6.5579
Chart: Speedup
| mandelbulbGPU | NBody | lbm | EigenValue | XSBench | Spmv | kmeans | swat | color | pb-bfs | mis | srad | lulesh | lud | hybridsort | Average
1 | 0.99784 | 0.99988 | 0.99822 | 1.0309 | 1.084 | 1.0915 | 1.0047 | 1.0291 | 1.069 | 1.0028 | 1.0292 | 1.0668 | 1.0822 | 1.0477 | 1.132 | 1.0444
10 | 0.99607 | 0.99978 | 0.99676 | 1.0572 | 1.164 | 1.1807 | 1.0086 | 1.0594 | 1.1266 | 1.0074 | 1.0545 | 1.132 | 1.1624 | 1.0939 | 1.2463 | 1.0857
100 | 0.99573 | 0.99976 | 0.99648 | 1.0625 | 1.1813 | 1.2002 | 1.0094 | 1.0662 | 1.1381 | 1.0088 | 1.0597 | 1.1463 | 1.18 | 1.104 | 1.2697 | 1.0945
Steady state | 0.99568 | 0.99976 | 0.99644 | 1.0632 | 1.1834 | 1.2026 | 1.0094 | 1.0671 | 1.1395 | 1.009 | 1.0603 | 1.1481 | 1.1822 | 1.1053 | 1.2725 | 1.0956

## Slide 53: Final Takeaway
MPC is a versatile scheme
  Does not hurt gains of regular benchmarks
  Improves energy savings
  Reduces performance loss
Online MPC reduces performance loss compared to traditional approaches
Online MPC is resilient to prediction inaccuracy due to
  Performance feedback
  MPC’s greedy and heuristic approximations depend minimally on prediction models
MPC does not need to look into entire future