## Slide 1: Top-pim: Throughput-Oriented Programmable Processing in Memory
Dong Ping Zhang, Nuwan Jayasena, Alex Lyashevsky
Joe Greathouse, Lifan Xu, Mike Ignatowski
AMD Research
25/06/14

## Slide 2: Processing-in-memory? HBM?

## Slide 3
$
Shared $
$
$
GPU
CPU
Core
CPU
Core
DRAM
Chart: Energy (pJ)
 | 50 | 14 | 560 | 594 | 20480 | 2048
Compute is cheap, Data movement is not
Source: ITRS, S. Keckler et al. [IEEE Micro, Sep-Oct. 2011],
T. Vogelsang [MICRO 2010], T. Farrell [Salishan 2014]

## Slide 4: Exascale computing challenges
Energy is the key limiter
  Exascale system
    At 4TB/s, vast majority of node energy could be consumed by the memory system
  10x reduction in memory energy
  25x improvement in system energy efficiency
  While improving performance
Need to rethink compute and memory organization
  Move computation closer to data
  Specialized support for bandwidth-intensive applications
Potential solution: processing-in-memory?
Today: ORNL Titan (node: AMD Opteron+Nvidia Tesla K20X)
2020: DOE FastForward RFP (issued May, 2012)
Source: ORNL, Nvidia, top500.org, LLNL
Chart: 
 | 250 | 4000
 | 54.848 | 1.5625
Peak Node Memory BW
4TB/s
~250GB/s
Memory Access Energy
> 50pJ/b
< 5pJ/b
Chart: 
 | 5.24 | 2.5
 | 2.1425 | 50
Compute/BW
Ratio
~5 FLOPS/B
System Energy Efficiency
50 GFLOPS/W
~2 GFLOPS/W
2.5 FLOPS/B
Memory hierarchy
Compute

## Slide 5: Outline
Background
  PIM prior work
  Die-stacking
PIM architecture and memory organization
Applications
  Graph apps, HPC apps, GPGPU benchmark
PIM performance and energy model
Evaluation of the PIM design choices
Conclusion and further research

## Slide 6: PIM research – in the past
Prior PIM research constrained by
  Implementation technology
  Non-traditional programming models
Examples of prior work:
  Integration of caches and computation
    “A logic-in-memory computer” (1970)
  Logic in DRAM processes
    In-memory processors with reduced performance or highly specialized
    Reduced DRAM due to presence of logic unit
  Embedded DRAM in logic processes
    Not cost-effective to have sufficient memory capacity, reduced DRAM density
Recent work:
  Micron’s Automata Processor
  3D stacked processor for accelerating 3D ultrasound beamformation
  Specialized in-stack processor to accelerate MapReduce workloads

## Slide 7: 3D Integration
Gabe Loh, 3D-Stacked Memory Architectures for Multi-Core Processors, ISCA 2008
www.cadence.com/Community/blogs/ii/archive/2013/01/22/cadence-imec-test-methodology-enables-3d-ic-memory-on-logic.aspx
http://www.engadget.com/2013/04/03/hybrid-memory-cube-receives-its-finished-spec/
Logic die under DRAM using TSVs
  Higher bandwidth, lower access power
Significant industry momentum
  Recent JEDEC standards (HBM, Wide I/O 2)
  Hybrid Memory Cube (HMC) consortjum
    Micron, Samsung, IBM, ARM, Xilinx, Altera etc.

## Slide 8: PIM research – new perspective
Initial focus: PIM under DRAM stack
DRAM
New opportunity: logic die stacked with memory
  Logic die needed anyway for signal redistribution and integrity
  Potential for non-trivial compute
Key benefits:
  Reduce bandwidth bottlenecks
  Improve energy efficiency
  Increase compute for a fixed interposer area
  Processor can be optimized for high BW/compute ratio
Challenges:
  Programming models and interfaces
  Architectural tradeoffs
  Application refactoring

## Slide 9: Guiding principles of AMD’s PIM research
Our focus
  3D die stacking
  Use base logic die(s) in memory stack
    General-purpose processors
    Support familiar programming models
Ease of use
  Support familiar programming models
  Build on HSA fundamentals
  Any processor (host or PIM) can access all memory on node
  No significant application change for host and PIM.
Broad applicability
  Across a broad range of applications
  Viable across multiple market segments
Logic die with PIM
Memory stack

## Slide 10: Baseline PIM architecture
An in-memory processor incorporated on the base die of each memory stack
No DRAM die stacked on host processor
An overview
Host
PIM &
DRAM controller
Memory dies
Abstract
load/store interface
Timing-specific
DRAM
interface

## Slide 11: Baseline PIM Architecture
GPU CUs provide compute throughput
CPU cores provide control and flexibility
Optional fixed-function accelerators
GPU CU Cluster(s)
X86
X86
GPU CU
CP
CPU Cluster(s)
X86 Cores
CPU Core
Fixed-Function
Hardware
X86 Cores
HW Accel.
Memory Switch
Stacked
Memory
Channel 0
Stacked
Memory
Channel 1
Stacked
Memory
Channel (n-1)
To/From
Host
Ctrl 0
Ctrl 1
Ctrl (n-1)
Base logic die of DRAM stack
To/From
Inter-PIM
Interconnect
DRAM or
NVRAM dies

## Slide 12: Explore breadth of Applicability of PIM
Broad set of kernels from HPC apps, graph algorithms, GPGPU benchmarks etc.
Analyzed using PIM GPU performance and energy models
Chart: Vector Instructions per second (millions)
| 7288.2003272309385 | 149098.72056234768 | 159960.15571129328 | 25618.45285335126 | 31037.195351117211 | 19964829.027409442 | 186319.55522076887 | 3775865.7328750803 | 2585974.8649040353 | 3495720.4815577697 | 73198511.387078673 | 7162832.9977931315 | 203367.20642369142 | 2584260.1340557686 | 3151.2628362129954 | 4456.7376123585236 | 4716.4791362369715 | 3144.0828361024555 | 290918.55785280559 | 714546.36489387904 | 1928252.1579931311
 | 103360214.363 | 1224959.7979 | 2750802.0646 | 78525614.1421 | 79636916.6371 | 8237220.8343 | 229001447.897 | 25857857.6248 | 610006.983 | 807368.3627 | 74614.4654 | 39792891.9196 | 38312901.881 | 588239.5511 | 57592.5191 | 89136718.7826 | 174148894.409 | 167685989.967 | 149280080.631 | 10933110.9923 | 1808180.8113
PF = ParticleFilter
SP = ShortestPath
RW = RandomWalk
LE = Leukocyte

## Slide 13: Why a new Simulator?
Why spend time building a new simulator when we could have used:
  SimNow, TSIM, gem5, Multi2Sim, MARSSx86, PTLsim, Zesto, FeS2, RSIM, ZSIM, Graphite, Flexus, SESC, SST, GPGPUSim, MacSim, Simics+GEMS, SimpleScalar……
Because they don’t answer the question we want to ask
  Runtime overhead too high
  Changes take too long to implement
  Memory overheads preclude large working sets
As a result: they can’t test the PIM design space on applications that matter
PIM Simulator trades off some accuracy for major performance improvements

## Slide 14: Challenges of modeling future systems
Large design space to explore
Heterogeneous Cores
Composition? Size? Speed?
Stacked Memories
Useful? Compute/BW Ratio? Latency? Capacity? Non-Volatile?
Thermal Constraints
Power Sharing? Heat dissipation? Sprinting?
Software Co-Design
New algorithms? Data placement? Programming models?
Ref: J. Greathouse et al. Simulation of Exascale Nodes through Runtime Hardware Monitoring, ModSim, 2013

## Slide 15: Challenges of modeling future systems
Need to run long enough to trigger interesting memory phenomena
  Working sets >> stacked memories of 100s of MB to multiple GB
Run long enough to observe power and thermal effects
  Example measured on a real heterogeneous processor
  ~2.5 trillion CPU instructions, ~60 trillion GPU operations
Applications of interest can be large
  Scaled studies can be challenging and misleading for complex applications
Why does simulator performance matter?
Chart: Time (seconds)
Ref: I. Paul et al., “Cooperative Boosting: Needy Versus Greedy Power Management”, ISCA 2013

## Slide 16: PIM Simulator Overview
Multi-Stage Performance Estimation Process
Phase 2
Phase 1
User Application
PIM Software Stack
Performance and Power Models
Trace Post-processor
Host Tasks
PIM Tasks
Commodity hardware
(CPU, GPU, APU)
OS (Linux)
Traces of HW and SW events related to performance and power
Machine Description
Performance & Power Estimates

## Slide 17: ML-based performance model
Execution time <--- F (architecture, application)
  Kernel time (and power) depends on:
    Underlying HW configuration
    Algorithms and data structures of the application
PIM GPU Architecture is represented by:
  Number of CUs (8, 16, 32)
  Processor frequency (500 – 100 – 1000 MHz)
  Memory Bandwidth (500 – 100 – 1300 MHz)
Application kernel is represented by feature vectors
  Dynamic CodeXL/Sprofile data, derived from HW counters.
Goals:
  Learn scaling pattern in offline training
  Estimate runtime and power for online prediction
162 design points

## Slide 18: Performance model – offline learning
1.75x Perf Gain
1.5x Perf Gain
Gathering data
  70 OpenCL kernels
  Each kernel: 162 hw configurations  162 pairs of execution time & performance counter feature vector

## Slide 19: Performance model
Feature vector: VALUUtilization, VALUBusy, SALUBusy, MemUnitBusy, MemUnitStalled, CacheHit, …
Offline learning – clustering of the scaling pattern
Online classification and prediction
  Classify the feature vector of the new kernel
  Performance projection with the scaling pattern of this cluster

## Slide 20: Performance model validation
69 training kernels; leave one kernel out  prediction  validation
    relative error between the prediction and real processing: accuracy verification
Make predictions for all other HW design points from each design point
    Variation of #CUs, bandwidth, engine frequency -> 162 operating points -> 162*161 (26K) data points on the 3D grid for each kernel!
Individual benchmark prediction errors
16.1%
Average prediction error - subset

## Slide 21: Technology and configurations
Evaluated for 22nm and 16nm
  Explore viability prior to Exascale timeframe
  Identify tech transfer opportunities
Design points and technology scaling
  PIM: limited by DRAM footprint and 10W/PIM
  Host: extrapolate current trends (assumes HMC-like DRAM interface)
 | Baseline | 22nm |  | 16nm | 
 | dGPU | Host | PIM | Host | PIM
Freq | 1GHz | 1GHz | 650MHz | 1GHz | 650MHz
Number of CUs | 32 | 32 | 8 | 64 | 12
Number of memory stacks |  | 2 |  | 4 | 
DRAM BW (GB/s) |  | 160 | 640 | 160 | 640
Dynamic power scaling | 1.00 | 0.61 | 0.25 | 0.41 | 0.17
Memory Energy (pJ/64b) |  | 522 | 159 | 520 | 155

## Slide 22: PIM can be performance-competitive with host
PF = ParticleFilter
SP = ShortestPath
RW = RandomWalk
Chart: PIM Performance /Host Performance
Config 1 - 22nm | 0.58098 | 0.325 | 1.0459 | 0.94167 | 0.61553 | 0.63912 | 0.67889 | 0.85927 | 0.48523 | 0.79531 | 1.3876 | 0.43634 | 0.94177 | 0.48635 | 0.77266 | 0.54834 | 0.41281 | 0.94505 | 0.87401 | 0.99366 | 0.53485 | 0.68465
Config 2 - 16nm | 1.2331 | 0.4875 | 1.3853 | 1.1587 | 1.2202 | 0.60402 | 0.68138 | 0.81072 | 0.9979 | 1.0599 | 1.7446 | 0.80797 | 0.91203 | 0.89461 | 1.1604 | 1.1323 | 0.81698 | 1.865 | 1.1431 | 1.3032 | 1.1019 | 1.0217
The higher, the better!
-27%
7%

## Slide 23: significant PERF/W improvements
Chart: PIM Perf/W Relative to Host
Config 1 - 22nm | 4.9718 | 2.7656 | 7.8513 | 7.1838 | 5.0718 | 12.1621 | 11.0557 | 14.2039 | 4.1722 | 5.278 | 9.7646 | 3.162 | 15.3664 | 3.6594 | 5.5075 | 4.2923 | 3.4043 | 7.2394 | 5.9772 | 6.5377 | 4.2662 | 6.8521
Config 2 - 16nm | 6.8985 | 2.7147 | 6.7428 | 5.8082 | 6.5745 | 15.0436 | 14.4443 | 17.5274 | 5.5933 | 4.6582 | 8.0763 | 3.8265 | 19.4658 | 4.3996 | 5.3115 | 5.7714 | 4.2591 | 8.9441 | 5.1562 | 5.6167 | 5.7447 | 7.7418
PF = ParticleFilter
SP = ShortestPath
RW = RandomWalk
The higher, the better!
6.9
7.7

## Slide 24: Conclusions and further research
“Computing” is increasingly about data and data movement
  Exploit locality to reduce wasteful data movement
  Specialization to improve efficiency
  PIM potentially provides significant reductions in off-chip traffic.
TOP-PIM implemented using 3D die-stacking feasible in near future.
  Efficiently utilize the high bandwidth available in local stack
  Programmability -> Support a broad range of applications
  Performance and energy efficiency of PIM vs Host
    At 22nm, 27% performance degradation, 76% reduction in EDP
    At 16nm, 7% performance gain, 85% reduction in EDP.
Future Work:
  High level programming models to express data-compute affinity.
  Data movement management and task scheduling for host and PIMs.
  Evaluation of alternative PIM organizations and design options.

## Slide 25: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2014 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. SPEC is a registered trademark of the Standard Performance Evaluation Corporation (SPEC). Other names are for informational purposes only and may be trademarks of their respective owners.