## Slide 1: Interference from GPU System Service Requests
Arkaprava Basu, Joseph L. Greathouse, Guru Venkataramani, JÁn VeselÝ
AMD Research, Advanced Micro Devices, Inc.

## Slide 2: Modern Systems are Powered by Heterogeneity
Machine Learning
Databases
Computer Vision
Regular Expressions
Physics
Graph Analytics
Finite State Machines
Genome Sequencing
Reconfigurable (e.g., FPGA)
6th Gen. AMD A-Series Processor “Carrizo”
CPUs
Video Decode
Video Encode
GPU
Accelerators from Industry and Academia

## Slide 3: Traditional Heterogeneous Computing Driven by CPUs
CPU
Data Transfer
Accelerator
Work launched by the CPU to accelerators
Data marshalled by the CPU
Communication and computation are coarse-grained

## Slide 4: Modern Accelerators are Equal Partners
CPU
Data Transfer
Accelerator
Accelerators and CPUs can launch work to one another (and themselves)
Data transfer implicit based on usage
Communication and computation are fine-grained

## Slide 5: Accelerators can now Request OS Services
GPU-to-CPU Callbacks (Owens et al., UCHPC 2010)
Page Faults / Demand Paging (Veselý et al., ISPASS 2016)
GPU-Initiated Network Requests (GPUnet, USENIX 2014)
GPU-Initiated File System Requests (GPUfs, ASPLOS 2013)
“Generic” System Calls (Genesys, ISCA 2018)
  ioctl() for other devices
  Memory management (e.g., sbrk(), mmap())
  Signals

## Slide 6: How a GPU System Service Request Is Handled
CPU 2
GPU
CPU 1
CPU 0
Memory
Step 1: Set up request arguments in memory
Step 2: Send request interrupt to a CPU
Step 3: (a) Schedule bottom-half handler
(b) ACK request to GPU
1
3b
3a
2

## Slide 7: How a GPU System Service Request Is Handled
CPU 2
GPU
CPU 1
CPU 0
Memory
1
3b
3a
4b
Step 4: (a) Set up kernel work queue arguments
(b) Queue worker thread
4a
2

## Slide 8: How a GPU System Service Request Is Handled
CPU 2
GPU
CPU 1
CPU 0
Memory
1
3b
3a
2
4b
4a
5
Step 5: Perform SSR
Step 6: Send response to GPU
6

## Slide 9: System Service Requests Can Lead to Difficulties
GPUs and accelerators can request OS (system) services
These SSRs can interfere with unrelated CPU-based work
Unrelated CPU-Based work can slow down GPU SSR handling
CPUs lose opportunity to sleep because of GPU SSRs

## Slide 10: Modes of Interference from GPU SSRs
1
2
3a
3b
4a
4b
5
6
CPU0
GPU
CPU1
CPU2
2
3
Mode/Task Switch
Kernel Task Operation
Low-Performance User-Mode Operation
CPU User Work
GPU User Work
3a
4
4b
GPU Stalls….
5

## Slide 11: Modes of Interference from GPU SSRs
CPU0
GPU
CPU1
CPU2
2
3
3a
4
4b
GPU Stalls….
5
Direct CPU Overheads
Indirect CPU Overheads
GPU Overheads

## Slide 12: Test Platform Used to Demonstrate this
AMD A10-7850K APU
  4x 3.7 GHz CPU cores. AMD Family 15h Model 30h
  720 MHz AMD GCN 1.1 (“Sea Islands”, gfx700) GPU, 8 CUs
  32 GB Dual-Channel DDR3-1866
Ubuntu 14.04.3 LTS (AMD64)
  Linux® kernel 4.0.0 with HSA Drivers (amdkfd 1.6.1)
PARSEC benchmarks for “CPU work”
OpenCL™ benchmark applications modified to create SSRs (page faults)
  BPT [Veselý et al., ISPASS 2016]
  XSBench [Veselý et al., ISPASS 2016]
  SHOC BFS
  SHOC SpMV
  Pannotia SSSP
  µBenchmark

## Slide 13: CPU Performance W/ SSR-Using GPU Applications

## Slide 14: Indirect CPU Overheads from GPU SSRs

## Slide 15: GPU Performance w/ Concurrent CPU Apps
CPU cores avoid going to sleep, which can increase responsiveness to GPU requests

## Slide 16
take inspiration from other domains (e.g. high performance Networking)
Mitigation Strategies
Interrupt Coalescing
Interrupt Steering
Merged SSR Handlers
Driver for Enforcing CPU QoS

## Slide 17: Mitigation: Interrupt Coalescing
1
2
3a
3b
4a
4b
5
6
CPU0
GPU
CPU1
CPU2
2
3
3a
4
4b
GPU Stalls….
5
Wait until multiple SSR requests arrive before interrupting CPU core
Take fewer interrupts and
see less indirect user-level overhead
But more likely to stall the GPU

## Slide 18: Mitigation: Interrupt Steering
1
2
3a
3b
4a
4b
5
6
CPU0
GPU
CPU1
CPU2
2
3
3a
4
4b
GPU Stalls….
5
Ensure that all interrupts go to the same core, rather than round-robin to all cores
Limit how many cores are affected. Reduce global indirect overheads.
But harms fairness!

## Slide 19: Mitigation: Merged SSR Handler
1
2
3a
3b
4a
4b
5
6
CPU0
GPU
CPU1
CPU2
2
3
3a
4
4b
GPU Stalls….
5
Merge SSR pre-proceeding (4) with interrupt handler (3)
Fewer interrupts and less indirect overhead.
Handle GPU requests with much less latency.
But runs more CPU code in high-priority context!

## Slide 20: Pareto Curve of Mitigation Strategy Tradeoffs
Interrupt Steering +
Merged Handler
Interrupt Steering + Interrupt Coalescing
Merged Handler
Default

## Slide 21: Driver Modifications To Ensure CPU QoS
CPU 2
GPU
CPU 1
CPU 0
Memory
1
3b
3a
2
4b
4a
5
6

## Slide 22: Driver Modifications To Ensure CPU QoS
CPU 2
GPU
CPU 1
CPU 0
Memory
1
3b
3a
2
4b
4a
5
Step 5: Track SSR overheads + delay step 6 to stall the GPU
Governor in Driver
6

## Slide 23: Governor to Control CPU QOS
CPU Cycles Handling SSRs > Threshold
Delay  0
Service SSR and Return GPU Result
Delay == 0?
Delay  10 µsec
Delay  Delay*2
Sleep ‘Delay’ µsec
Y
Y
N
N

## Slide 24: CPU Performance at Different QOS Levels

## Slide 25: GPU Performance Suffers for CPU QOS

## Slide 26: Summary
Heterogeneous systems can include increasingly more accelerators
GPUs and accelerators now request system services
These can cause interference between accelerators & unrelated CPU work
Problem may worsen in the future
Existing mitigation strategies help, but are not complete solution

## Slide 27
Questions?
Disclaimer
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
AMD, the AMD Arrow logo, and combinations thereof are trademarks of Advanced Micro Devices, Inc. Linux is a registered trademark of Linus Torvalds. OpenCL is a trademark of Apple Inc. used by permission by Khronos. Other names used herein are for identification purposes only and may be trademarks of their respective companies.

## Slide 28
Backup Slides

## Slide 29: Pareto Curve of Mitigation Strategy Tradeoffs
Default
Interrupt Steering
Merged Handler
Merged Handler + Interrupt Steering
Interrupt Steering + Interrupt Coalescing
Merged Handler + Interrupt Steering + Coalescing
Merged Handler + Interrupt Coalescing
Interrupt Coalescing

## Slide 30: SSRs Limit Low-Power Sleep States

## Slide 31: Mitigation Effect on Sleep States