## Slide 1: Testudo: Heavyweight Security Analysis via Statistical Sampling
Joseph L. Greathouse
Advanced Computer Architecture Laboratory
University of Michigan
Ilya Wagner
David A. Ramos
Gautam Bhatnagar
Todd Austin
Valeria Bertacco
Seth Pettie
MICRO, Lake Como, Italy
November 11, 2008
Notes: Good morning everyone. I’m Joseph Greathouse, and I will be discussing Testudo, a system for heavyweight security analysis via statistical sampling.

## Slide 2: Bad Software is Everywhere
NIST: SW errors cost U.S. $60 billion/year as of 2002
These errors include security vulnerabilities.
"Security bugs are out there, in fact in web apps they're pretty much a plague.” - Zeev Suraski, co-creator of PHP
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 (proj.)
Security Reports | 1090 | 2437 | 4129 | 3784 | 3780 | 5990 | 8064 | 7236 | 8077.3333
CERT-Cataloged Vulnerabilities
Notes: I’m here because bad software is everywhere. As proof: the u.s. national institute of standards and technology reported that as of the year 2002, software errors cost the U.S. economy alone $60 billion per year. While not all of these problems were security vulnerabilities, security problems still make up a large, and dangerous, group of software errors.
In fact, Zeev Suraski, one of the co-creators of PHP, has called bugs not just a problem, but a plague.
Proof of that assertion can be seen in these statistics from CERT, the computer emergency response team, a group that catalogs security vulnerabilities on the internet. In the year 2002, when the $60 bil/year estimate was made, there were about 4000 newly-published security vulnerabilities. This year, we’re on track to see over 8000.
In fact, if you use Gentoo Linux, you were just affected by a security bug in a kernel driver last week. Microsoft just released an unscheduled patch for a severe security hole three weeks ago. And if you needed a passport to make it to MICRO, you may have used a passport reader that was affected by a severe security vulnerability.

## Slide 3: Software Dynamic Analysis for Security
Valgrind, Rational Purify, DynInst
  Multiple types of tests, runtime protection
  Extremely high runtime overheads
Developer
Program
Instrumented Program
In-House
Test Server(s)
LONG run time
Analysis Results
Analysis Instrumentation
Notes: So because these problems are so numerous, there has been a great deal of work on methods to combat them. I’d like to focus on one class of methods that has seen a lot of recent work: dynamic analyses.
Dynamic analyses are security checks that are performed while the program is running, allowing the developer to monitor the runtime state of the program and use that information to reason about the safety of the process.
The current way that dynamic analyses are used is through software instrumentation tools like Valgrind, IBM Rational Purify, and DynInst. These tools instrument the software, which allows it to perform tests on itself at runtime. They offer a wide variety of tests, from simple taint checking to dynamic bounds checking and beyond. They also offer the benefit of runtime protection against security attacks, since a program that knows it is being exploited can stop before bad things happen. However, this benefit is counteracted by the extremely high runtime overheads incurred by software dynamic analysis. These overheads are on the orders of 20x, 30x, or 200x.
Because of these runtime overheads, a developer that wishes to use dynamic analysis on his program will probably use it in a manner like this:
This developer starts with his program, and sends it through some kind of instrumentation tool. It comes out larger, due to carrying the analysis instrumentation along. It then will run on some kind of in-house test server. Because of the extremely long runtimes, this instrumented version of the program will never go out to users.
After this long runtime, the developer gets back the analysis results, both positive and negative. However, because dynamic analysis relies on the runtime state of the system, the developer may want to run more tests with different inputs. Once again, the long runtimes make this prohibitive.

## Slide 4: Hardware Dynamic Analysis for Security
DIFT, Raksha, FlexiTaint, et al.
  Low/no runtime overhead, runtime protection
  Limited analysis types, complex HW overhead
In-House
Test Server(s)
Developer
Hardware-Instrumented
Test Server(s)
Program
Analysis Results
Notes: That’s where research in the hardware community comes in. Recent work on solving overhead problem.

## Slide 5: Testudo: Distributed Dynamic Analysis
Users running at full speed
Reported before they are exploited
Split analysis across population of users
  Low HW cost, low runtime overhead, runtime information from the field
  Analysis only
Developer
Instrumented Program
Potential problems encountered

## Slide 6: Heavyweight Dynamic Analysis
Heavyweight analyses use shadow values.
Shadow values hold meta-information about associated memory values
Can be used to detect potential errors without an active exploit.
6
Memory Location
Shadow Value
Data
Meta-Data:
Trusted/Untrusted
Maximum/Minimum
Symbolic Information

## Slide 7: Example of Heavyweight Analysis
I/O
x=read_in()
y = x + 1
z = x * 2
int sample(int a[8]){
int x = read_in();
int y = x + 1;
int z = x * 2;
print a[x];
if(y>0&&y<8)
print a[y];
return a[z];
}
Key:
= has shadow value
Dataflow:
Code:
Memory Location
Shadow Value
Memory:
a[0]
x
y
z
6
UT
7
UT
UT
12
T

## Slide 8: Contributions of Testudo
Reduce hardware complexity: Shadow storage is a small, constant size. No out-of-core changes.
Reduce runtime overhead: Divide work across users to reduce overhead for each individual.
Increase analysis quality: Large user population allows analysis of large, varying state spaces.

## Slide 9: Dataflow Sampling Example: 1st User
x=read_in()
y = x + 1
z = x * 2
int sample(int a[8]){
int x = read_in();
int y = x + 1;
int z = x * 2;
print a[x];
if(y>0&&y<8)
print a[y];
return a[z];
}
Dataflow:
Code:
Memory Location
Single shared shadow value
Memory:
a[0]
x
y
z
6
7
12
Key:
*
= shadow value
= no shadow value
= globally observed shadow value
UT
No Replacement
I/O
*

## Slide 10: Dataflow Sampling Example: 2nd User
x=read_in()
y = x + 1
z = x * 2
int sample(int a[8]){
int x = read_in();
int y = x + 1;
int z = x * 2;
print a[x];
if(y>0&&y<8)
print a[y];
return a[z];
}
Dataflow:
Code:
Memory Location
Single shared shadow value
Memory:
a[0]
x
y
z
6
7
12
Key:
*
= shadow value
= no shadow value
= globally observed shadow value
UT
I/O
*
*
x=read_in()
T

## Slide 11: Dataflow Sampling Example: 3rd User
z = x * 2
x=read_in()
y = x + 1
int sample(int a[8]){
int x = read_in();
int y = x + 1;
int z = x * 2;
print a[x];
if(y>0&&y<8)
print a[y];
return a[z];
}
Dataflow:
Code:
Memory Location
Single shared shadow value
Memory:
a[0]
x
y
z
6
7
12
Key:
*
= shadow value
= no shadow value
= globally observed shadow value
UT
No Replacement
I/O
*
*
*
x=read_in()

## Slide 12: A Pipeline for Testudo
WB
MEM
EX
ID
IF
Instruction Decode
Register File
Shadow Values
Extend registers with single shadow bit.
Also extend pipeline buffers.
Common in hardware DIFT
S
Regs

## Slide 13: A Pipeline for Testudo
WB
MEM
EX
ID
IF
Compute new shadow bits
Generally hard-coded in some way
Common in hardware DIFT
Execution Stage
S
Regs
Calc

## Slide 14: A Pipeline for Testudo
WB
MEM
EX
ID
IF
Contains addresses of shadowed variables
Drop some values when this small cache is full
Replacement scheme not deterministic
S
Regs
Memory Stage
Sample Cache
Shadowed Location
Calc
Sample
Cache

## Slide 15: A Pipeline for Testudo
WB
MEM
EX
ID
IF
Different actions & opcodes lead to different handler code
Replaces or augments EX-stage modifications
Allows for complicated testing and propagation
S
Regs
Calc
Sample
Cache
Write Back
Policy Map
opcode
Handler address
Policy Map

## Slide 16: Experimental Framework
Insecure programs (with exploits), including:
  TIFF image engine
  Eggdrop IRC bot
  Lynx web browser
  PDF library
  Simulated SQL injection
CACTI v5.0 used for cache estimation.
Modified Virtutech Simics
+ Modified Bochs x86 emulator
Custom Sample Cache Simulator
Shadow value traces

## Slide 17: How many runs will I need?
To see all of a program’s dataflows with high statistical confidence.
Some need few samples with tiny sample caches
Chart: 
| tiff | eggdrop | lynx
 | 121 | 32 | 45
Chart: 
| tiff | eggdrop | lynx
 | 75 | 25 | 32
32-entry cache
64-entry cache
Avg. # of executions
Others need a larger cache and/or more runs for good results
Chart: 
| pdf | sql_injct
 | 3000 | 18000
Avg. # of executions
512-entry cache
Chart: 
| pdf | sql_injct
 | 2300 | 3600
1024-entry cache
17601

## Slide 18: Does it scale to complex analyses?
If each shadow operation uses 1000 instructions:
Chart: 
| pdf | sql_injct
 | 0.19388 | 0.1949
Average % Overhead
1024-entry Sample Cache
Each execution sees few shadow values
Chart: 
| 1024 entry | 512 entry
 | 17.3303 | 0.34779
Average % Overhead
telnet server benchmark
Fewer shadow values reduce overhead
%
%
3500 executions
17.3%
0.3%
169,000 executions
Tradeoff: need more executions

## Slide 19: How much will it cost?
~0 change in clock period of modern CPU
No overhead outside of the CPU core
Very low hardware overhead in CPU core
Sample Cache Access Time
% Increase of Core+L1
Chart: 
| 256 entry | 512 entry | 1024 entry | 1024 entry
 | 73 | 85 | 90 | 98
% of CPU Cycle
2.5GHz AMD Phenom
1.4GHz UltraSPARC T2
Chart: 
| 256 entry | 512 entry | 1024 entry | 1024 entry
 | 0.15 | 0.26 | 0.43 | 0.88
AMD Phenom
UltraSPARC T2
Sample Cache Area Overhead
Notes: Why cache access is so short: cache is very small

## Slide 20: Conclusions from Testudo
Simplified hardware design for dynamic analysis
Reduced runtime overhead for heavyweight security analysis
Increased heavyweight dynamic analysis quality
Future Directions
Adapting Testudo hardware for multicore
What is the best cache replacement method?
Can we skip the hardware additions?

## Slide 21
Thank you

## Slide 22: BACKUP SLIDES
Picture rights:
  One of the following Testudo pictures has been removed, but I don’t remember which one.
Testudo picture 1 http://www.flickr.com/photos/frield/1254958611/
Testudo picture 2 http://www.flickr.com/photos/manel/154985772/
'The Art of Debugging ...' and 'The IDA Pro Book': http://nostarch.com/
Fuzzing for Software Security Testing and Quality Assurance http://www.artechhouse.com/Detail.aspx?strIsbn=978-1-59693-214-2
Secure Programming with Static Analysis copyright Addison-Wesley

## Slide 23: Systems for Detecting Security Errors
Eyeballs
  Disassembly, debugging, fuzz testing, whitehat/grayhat hackers
  Time-consuming, difficult
Static Analysis
  Analyze source, formal reasoning methods, compile-time checks
  Intractable, requires expert input, no system state

## Slide 24: Security Vulnerability Example
Buffer overflows a large class of security vulnerabilities
void foo()
{
int local_variables;
int buffer[256];
…
buffer = read_input();
…
return;
}
Return address
Local variables
buffer
Buffer Fill
New Return address
Bad Local variables
If read_input() reads 200 ints
If read_input() reads >256 ints
buffer

## Slide 25: Testudo–Distributed Dynamic Debugging
Developer
Analyses
Program
Users running at full speed
Problems reported
before they’re exploited
Testudo: Heavyweight Sampling Analysis
Developer
Analyses
Program
In-House
Test Server(s)
LONG runtimes
Current Heavyweight Analysis Systems

## Slide 26: Example Dataflow
I/O
x=read_input()
y = x * 1024
z = x + 42
a += y
z = y * 75
y++
void function(int &y, int &z, int &a)
{
int x = read_input();
y = x*1024;
a += y;
z = y * 75;
…
y++;
z = x+42;
return;
}
Key:
= has shadow value

## Slide 27: Sampling of a Dataflow
I/O
x=read_input()
y = x * 1024
z = x + 42
a += y
z = y * 75
y++
HW limitations force us to ignore some shadow value stores
void function(int &y, int &z, int &a)
{
int x = read_input();
y = x*1024;
a += y;
z = y * 75;
…
y++;
z = x+42;
return;
}
x=read_input()
z = x + 42
1st execution:
*
*
Key:
= has shadow value
= no shadow value
= globally observed shadow value
*

## Slide 28: Sampling of a Dataflow
I/O
x=read_input()
y = x * 1024
z = x + 42
a += y
z = y * 75
y++
void function(int &y, int &z, int &a)
{
int x = read_input();
y = x*1024;
a += y;
z = y * 75;
…
y++;
z = x+42;
return;
}
2nd execution:
x=read_input()
*
*
y = x * 1024
a += y
z = y * 75
*
*
*
Key:
= has shadow value
= no shadow value
= globally observed shadow value
*

## Slide 29: Sampling of a Dataflow
void function(int &y, int &z, int &a)
{
int x = read_input();
y = x*1024;
a += y;
z = y * 75;
…
y++;
z = x+42;
return;
}
I/O
x=read_input()
y = x * 1024
z = x + 42
a += y
z = y * 75
y++
3rd execution:
x=read_input()
*
*
y = x * 1024
z = x + 42
*
*
*
y++
Key:
= has shadow value
= no shadow value
= globally observed shadow value
*
*

## Slide 30: Sampling of a Dataflow
I/O
x=read_input()
y = x * 1024
z = x + 42
a += y
z = y * 75
y++
void function(int &y, int &z, int &a)
{
int x = read_input();
y = x*1024;
a += y;
z = y * 75;
…
y++;
z = x+42;
return;
}
3rd execution:
x=read_input()
*
*
y = x * 1024
z = x + 42
*
*
*
y++
Key:
= shadow value
= no shadow value
= globally observed shadow value
*
*