## Slide 1: Simulation of exascale nodes through runtime hardware monitoring
Joseph L. Greathouse, alexander lyashevsky, mitesh meswani, nuwan Jayasena, Michael Ignatowski
9/18/2013

## Slide 2: Challenges of exascale node research
Many design decisions
Heterogeneous Cores
Composition? Size? Speed?
Stacked Memories
Useful? Compute/BW Ratio? Latency? Capacity? Non-Volatile?
Thermal Constraints
Power Sharing? Heat dissipation? Sprinting?
Software Co-Design
New algorithms? Data placement? Programming models?
Exascale: Huge Design Space to Explore
Notes: Heterogeneous Chip Picture from: Sebastien Nussbaum’s “AMD ‘Trinity’ APU,” Hot Chips 2012
Stacked Memory Picture from: Gabe Loh’s “3D-Stacked Memory Architectures for Multi-Core Processors,” ISCA 2008
Thermal Picture from: Indrani Paul’s “Cooperative Boosting: Needy versus Greedy Power Management,” ISCA 2013
Code snippet from the OpenCL version of LULESH.

## Slide 3: Challenges of Exascale Node Research
Power and Thermals on a real heterogeneous processor:
  ~2.5 trillion CPU instructions, ~60 trillion GPU operations
Exascale Proxy Applications are Large
  Large initialization phases, many long iterations
  Not microbenchmarks
  Already reduced inputs and computation from real HPC applications
Interesting Question Require Long Runtimes
Chart: Time (seconds)
Exascale: Huge Execution Times
Notes: Chart from Indrani Paul’s, “Cooperative Boosting: Needy versus Greedy Power Management,” ISCA 2013
Instruction counts:
  6 minutes * 60s/min * 4 cores * ~1.75GHz (A8-4555M)
  6 minutes * 60s/min * 6 CUs * 64 floating point units/CU * ~425MHz (Radeon HD 7600G)

## Slide 4: Existing Simulators
Microarchitecture Sims: e.g. gem5, Multi2Sim, MARSSx86, SESC, GPGPU-Sim
  Excellent for low-level details. We need these!
  Too slow for design space explorations: ~60 trillion operations = 1 year of sim time
Functional Simulators: e.g. SimNow, Simics, QEMU, etc.
  Faster than microarchitectural simulators, good for things like access patterns
  No relation to hardware performance
High-Level Simulators: e.g. Sniper, Graphite, CPR
  Break operations down into timing models, e.g. core interactions, pipeline stalls, etc.
  Faster, easier to parallelize.
  Runtimes and complexity still constrained by desire to achieve accuracy.
Notes: 1 year of SIM time assumes ~2 MIPS for an entire year.
SST: Structural Simulation Toolkit
CPR: Composable Performance Regression

## Slide 5: Trade off individual test accuracy
Doctors do not start with:
Notes: CAT Scan Photo Attribution: Flickr user “Muffet” -- http://www.flickr.com/photos/calliope/361953316/ . Used under CC BY.
Chest X-Ray Attribution: Flickr user “Aidan Jones” -- http://www.flickr.com/photos/aidan_jones/1438403889/ Used under CC BY-SA.
Microscope Attribution: Flickr user “Elsie esq.” -- http://www.flickr.com/photos/elsie/7080667207/ Used under CC BY.

## Slide 6: Fast Simulation Using Hardware Monitoring

## Slide 7: High-Level Simulation Methodology
Multi-Stage Performance Estimation Process
Phase 2
Phase 1
User Application
Simulator Software Stack
Performance, Power, and Thermal Models
Trace Post-processor
Software Tasks
Test System APU, CPU, GPU
Test System OS
Traces of HW and SW events related to performance and power
Machine Description
Performance & Power Estimates

## Slide 8: Benefits of multi-step process
Many design space changes only need second step
Phase 2
Phase 1
User Application
Simulator Software Stack
Performance, Power, and Thermal Models
Trace Post-processor
Software Tasks
Test System APU, CPU, GPU
Test System OS
HW & SW Traces
Multiple Machine Descriptions
Performance & Power Estimates

## Slide 9: Performance Scaling a Single-Threaded App
Current Processor
Gather statistics and performance counters about:
  Instructions Committed, stall cycles
  Memory operations, cache misses, etc.
  Power usage
Simulated Processor
Start Time
End Time
Analytical Performance Scaling Model
New
Runtime
Time

## Slide 10: Analytic Performance Scaling
CPU Performance Scaling:
  Find stall events using HW perf. counters. Scale based on new machine parameters.
  Large amount of work in the literature on DVFS performance scaling, interval models..
  Some events can be scaled by fiat: “If IPC when not stalled on memory doubled, what would happen to performance?”
GPU Performance Scaling:
  Watch HW perf. counters that indicate work to do, memory usage, and GPU efficiency
  Scale values based on estimations of parameters to test
Notes: “Based on what this application did, what will it do on our future machine?”
GPU Example: e.g. Entire citation: Jaewoong Sim, Aniruddha Dasgupta, Hyesoon Kim, Richard W. Vuduc: A performance analysis framework for identifying potential benefits in GPGPU applications. At PPoPP 2012.

## Slide 11: Other analytic models
Cache/Memory Access Model
  Observe memory access traces using binary instrumentation or hardware
  Send traces through high-level cache simulation system
  Find knees in the curve, feed this back to CPU/GPU performance scaling model
Power and thermal models
  Power can be correlated to hardware events or directly measured
  Scaled to future technology points
  Any number of thermal models will work at this point
Thermal and power models can feed into control algorithms that change system performance
  This is another HW/SW co-design point. Fast operation is essential.

## Slide 12: Scaling Parallel Segments Requires More Info
CPU0
Time
CPU1
GPU
Example when everything except CPU1 gets faster:
Performance Difference
CPU0
CPU1
GPU

## Slide 13: Must reconstruct critical paths
Gather program-level relationship between individually scaled segments
Use these happens-before relationships to build a legal execution order
Gather ordering from library calls like pthread_create() and clWaitForEvents()
Can also split segments based on program phases
CPU0
CPU1
GPU
①
②
⑦
⑥
③
④
⑤

## Slide 14: Conclusion
Exascale node design space is huge
Trade off some accuracy for faster simulation
Use analytic models based on information from existing hardware

## Slide 15: Research Related Questions

## Slide 16: MODSIM Related Questions
Major Contributions:
  A fast, high-level performance, power, and thermal analysis infrastructure
  Enables large design space exploration and HW/SW co-design with good feedback
Limitations:
  Trace-based simulation has known limitations w/r/t multiple paths of execution, wrong-path operations, etc.
  It can be difficult and slow to model something if your hardware can’t measure values that are correlated to it.
Bigger Picture:
  Node-level performance model for datacenter/cluster performance modeling
  First pass model for APU power sharing algorithms.
  Exascale application co-design
  Complementary work to broad projects like SST
Notes: what is the major contribution of your research?
*what are the gaps you identify in the research coverage in your area?
*what is the bigger picture for your research area? (i.e., identify synergistic projects, complementary projects in technical sense, etc)
*how do you see cross-pollination across projects funded by different funding agencies?
*what is the one thing that would make it easier/possible to leverage/use the results of other projects to further your own research
*what would you like to most see solved/addressed other than what they are working on?

## Slide 17: MODSIM Related Questions
What is the one thing that would make it easier to leverage the results of other projects to further your own research
  Theoretical bounds and analytic reasoning behind performance numbers. Even “good enough” guesses may help, vs. only giving the output of a simulator
What are important thing to address in future work?
  Better analytic scaling models. There are a lot in the literature, but many rely on simulation to propose new hardware that would gather correct statistics.
  It would be great if open source performance monitoring software were better funded, had more people, etc.

## Slide 18: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2013 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. Other names are for informational purposes only and may be trademarks of their respective owners.

## Slide 19: Backup

## Slide 20: An Exascale Node Example Question
Is 3D-Stacked Memory Beneficial for Application X?
Baseline Performance
Bandwidth Difference
Latency Difference
Thermal Model
Core Changes due to Heat
Simulation Run(s)
Redesign
Modify software to better utilize new hardware
Performance results based on design point(s)