## Slide 1: Accelerating Dynamic Software Analyses
Joseph L. Greathouse
Ph.D. Candidate
Advanced Computer Architecture Laboratory
University of Michigan
December 2, 2011
Notes: This talk was given at Microsoft Research in Silicon Valley on December 2, 2011. (Thanks to John Davis). This is basically a mix of my CGO 2011 talk along with my ISCA 2011 talk. See those slides for detailed notes of what all the animations mean.

## Slide 2: Software Errors Abound
NIST: SW errors cost U.S. ~$60 billion/year as of 2002
FBI CCS: Security Issues $67 billion/year as of 2005
  >⅓ from viruses, network intrusion, etc.
Cataloged Software Vulnerabilities
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008
CVE Candidates | 1246 | 1587 | 2434 | 1596 | 2769 | 4889 | 7245 | 6743 | 7291
CERT Vulnerabilities | 1090 | 2437 | 4129 | 3784 | 3780 | 5990 | 8064 | 7236 | 8077

## Slide 3: Example of a Modern Bug
Thread 2
mylen=large
Thread 1
mylen=small
ptr
∅
Nov. 2010 OpenSSL Security Flaw
if(ptr == NULL) {
len=thread_local->mylen;
ptr=malloc(len);
memcpy(ptr, data, len);
}

## Slide 4: Example of a Modern Bug
if(ptr==NULL)
if(ptr==NULL)
memcpy(ptr, data2, len2)
ptr
LEAKED
TIME
Thread 2
mylen=large
Thread 1
mylen=small
∅
len2=thread_local->mylen;
ptr=malloc(len2);
len1=thread_local->mylen;
ptr=malloc(len1);
memcpy(ptr, data1, len1)

## Slide 5: Dynamic Software Analysis
Analyze the program as it runs
  System state, find errors on any executed path
  LARGE runtime overheads, only test one path
Developer
Instrumented Program
In-House
Test Machine(s)
LONG run time
Analysis Results
Analysis Instrumentation
Program

## Slide 6: Runtime Overheads: How Large?
Taint Analysis (e.g.TaintCheck)
Dynamic Bounds Checking
Data Race Detection (e.g. Inspector XE)
Memory Checking (e.g. MemCheck)
2-200x
10-80x
5-50x
2-300x
Symbolic Execution
10-200x

## Slide 7: Outline
Problem Statement
Background Information
  Demand-Driven Dynamic Dataflow Analysis
Proposed Solutions
  Demand-Driven Data Race Detection
  Sampling to Cap Maximum Overheads

## Slide 8: Dynamic Dataflow Analysis
Associate meta-data with program values
Propagate/Clear meta-data while executing
Check meta-data for safety & correctness
Forms dataflows of meta/shadow information

## Slide 9: Example: Taint Analysis
a += y
z = y * 75
y = x * 1024
w = x + 42
Check w
Check w
validate(x)
x = read_input()
Clear
a += y
z = y * 75
y = x * 1024
x = read_input()
Propagate
Associate
Input
Check a
Check a
Check z
Check z
Data
Meta-data

## Slide 10: Demand-Driven Dataflow Analysis
Only Analyze Shadowed Data
Native
Application
Instrumented Application
Instrumented
Application
Meta-Data Detection
Non-Shadowed Data
Shadowed Data
No meta-data

## Slide 11: Finding Meta-Data
No additional overhead when no meta-data
  Needs hardware support
Take a fault when touching shadowed data
Solution: Virtual Memory Watchpoints
V→P
V→P
FAULT

## Slide 12: Results by Ho et al.
lmbench Best Case Results:
Results when everything is tainted:
System | Slowdown (normalized)
Taint Analysis | 101.7x
On-Demand Taint Analysis | 1.98x
Chart: Slowdown (x)
| netcat_transmit | netcat_receive | ssh_transmit | ssh_receive
 | 164.184 | 13.1648 | 130.4188 | 113.9884

## Slide 13: Outline
Problem Statement
Background Information
  Demand-Driven Dynamic Dataflow Analysis
Proposed Solutions
  Demand-Driven Data Race Detection
  Sampling to Cap Maximum Overheads

## Slide 14: Software Data Race Detection
Add checks around every memory access
Find inter-thread sharing events
Synchronization between write-shared accesses?
  No? Data race.

## Slide 15: Example of Data Race Detection
Thread 2
mylen=large
Thread 1
mylen=small
if(ptr==NULL)
if(ptr==NULL)
len1=thread_local->mylen;
ptr=malloc(len1);
memcpy(ptr, data1, len1)
len2=thread_local->mylen;
ptr=malloc(len2);
memcpy(ptr, data2, len2)
ptr write-shared?
Interleaved Synchronization?
TIME

## Slide 16: SW Race Detection is Slow
Chart: Race Detector Slowdown (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean | blackscholes | bodytrack | facesim | ferret | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
 | 48.1483 | 98.4291 | 261.2096 | 278.4874 | 121.3327 | 28.0403 | 23.5499 | 83.2106 | 28.465 | 119.353 | 103.9687 | 80.0587 | 123.4686 | 5.3481 | 65.9072 | 137.1643 | 164.4939 | 109.1232 | 36.2791 | 99.1297 | 207.8853 | 74.7261
Phoenix
PARSEC

## Slide 17: Inter-thread Sharing is What’s Important
“Data races ... are failures in programs that access and update shared data in critical sections” – Netzer & Miller, 1992
if(ptr==NULL)
if(ptr==NULL)
len1=thread_local->mylen;
ptr=malloc(len1);
memcpy(ptr, data1, len1)
len2=thread_local->mylen;
ptr=malloc(len2);
memcpy(ptr, data2, len2)
Thread-local data
NO SHARING
Shared data
NO INTER-THREAD SHARING EVENTS
TIME

## Slide 18: Very Little Inter-Thread Sharing
Phoenix
PARSEC
Chart: % Write-Sharing Events
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | blackscholes | bodytrack | facesim | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster
 | 7.9849e-05 | 0.001152 | 2.3676e-05 | 8.4683e-06 | 1.9398e-05 | 7.4788e-05 | 0.024552 | 0.00036515 | 1.2408 | 0.24109 | 0.60989 | 0.00067053 | 0.22956 | 0.086346 | 0.54613 | 0.48584 | 0.19271 | 2.884 | 0.18591

## Slide 19: Use Demand-Driven Analysis!
Multi-threaded
Application
Software Race Detector
Software Race Detector
Local Access
Inter-thread sharing
Inter-thread Sharing Monitor

## Slide 20: Finding Inter-thread Sharing
Virtual Memory Watchpoints?
  ~100% of accesses cause page faults
Granularity Gap
Per-process not per-thread
FAULT
FAULT
Inter-Thread Sharing

## Slide 21: Hardware Sharing Detector
Hardware Performance Counters
Intel’s HITM event: W→R Data Sharing
S
M
S
I
HITM
Pipeline
Cache
0
0
0
0
Perf. Ctrs
1
2
1
-1
FAULT
Core 1
Core 2
-
-
-
-
PEBS
Armed
Debug Store
EFLAGS
EIP
RegVals
MemInfo
Precise
Fault

## Slide 22: Potential Accuracy & Perf. Problems
Limitations of Performance Counters
  HITM only finds W→R Data Sharing
  Hardware prefetcher events aren’t counted
Limitations of Cache Events
  SMT sharing can’t be counted
  Cache eviction causes missed events
  False sharing, etc…
PEBS events still go through the kernel

## Slide 23: Demand-Driven Analysis on Real HW
Execute Instruction
SW Race Detection
Enable Analysis
Disable Analysis
HITM
Interrupt?
Sharing Recently?
Analysis
Enabled?
NO
NO
NO
YES
YES
YES

## Slide 24: Performance Increases
Chart: Demand-driven Analysis Speedup (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean | blackscholes | bodytrack | facesim | ferret | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
 | 7.7361 | 8.1072 | 15.697 | 51.0497 | 11.269 | 3.1648 | 5.4724 | 9.9724 | 5.2325 | 7.6767 | 4.8782 | 3.3103 | 13.4522 | 1.5827 | 2.2085 | 2.3516 | 1.2223 | 3.184 | 2.1277 | 1.8448 | 1.2331 | 2.962
Phoenix
PARSEC
51x

## Slide 25: Demand-Driven Analysis Accuracy
Chart: Demand-driven Analysis Speedup (x)
| histogram | kmeans | linear_regression | matrix_multiply | pca | string_match | word_count | GeoMean | blackscholes | bodytrack | facesim | ferret | freqmine | raytrace | swaptions | fluidanimate | vips | x264 | canneal | dedup | streamcluster | GeoMean
 | 7.7361 | 8.1072 | 15.697 | 51.0497 | 11.269 | 3.1648 | 5.4724 | 9.9724 | 5.2325 | 7.6767 | 4.8782 | 3.3103 | 13.4522 | 1.5827 | 2.2085 | 2.3516 | 1.2223 | 3.184 | 2.1277 | 1.8448 | 1.2331 | 2.962
1/1
2/4
3/3
4/4
3/3
4/4
4/4
2/4
4/4
4/4
2/4
Accuracy vs. Continuous Analysis: 97%

## Slide 26: Outline
Problem Statement
Background Information
  Demand-Driven Dynamic Dataflow Analysis
Proposed Solutions
  Demand-Driven Data Race Detection
  Sampling to Cap Maximum Overheads

## Slide 27: Reducing Overheads Further: Sampling
Lower overheads by skipping some analyses
Chart: Overhead
| 0 | 25 | 50 | 75 | 100
 | 0 | 25 | 50 | 75 | 100
Complete Analysis
No
Analysis

## Slide 28: Sampling Allows Distribution
Chart: Overhead
| 0 | 25 | 50 | 75 | 100
 | 0 | 25 | 50 | 75 | 100
Developer
Beta Testers
End Users
Many users testing at little overhead see more errors than one user at high overhead.

## Slide 29: Cannot Naïvely Sample Code
a += y
z = y * 75
y = x * 1024
w = x + 42
Validate(x)
x = read_input()
a += y
y = x * 1024
False Positive
False Negative
w = x + 42
validate(x)
x = read_input()
Skip Instr.
Input
Check w
Check w
Check z
Check z
Skip Instr.
Check a
Check a

## Slide 30: Solution: Sample Data, not Code
Sampling must be aware of meta-data
Remove meta-data from skipped dataflows
  Prevents false positives

## Slide 31: Dataflow Sampling Example
a += y
z = y * 75
y = x * 1024
w = x + 42
validate(x)
x = read_input()
a += y
y = x * 1024
False Negative
x = read_input()
Skip Dataflow
Input
Check w
Check w
Check z
Check z
Skip Dataflow
Check a
Check a

## Slide 32: Dataflow Sampling
Remove dataflows if execution is too slow
Sampling Analysis Tool
Instrumented
Application
Native Application
Instrumented
Application
Meta-Data Detection
Meta-data
Clear meta-data
OH Threshold

## Slide 33: Prototype Setup
Taint analysis sampling system
  Network packets untrusted
Xen-based demand analysis
  Whole-system analysis with modified QEMU
Overhead Manager (OHM) is user-controlled
Xen Hypervisor
OS and Applications
App
App
App
…
Linux
ShadowPage Table
Admin VM
Taint Analysis QEMU
Net Stack
OHM

## Slide 34: Benchmarks
Performance – Network Throughput
  Example: ssh_receive
Accuracy of Sampling Analysis
  Real-world Security Exploits
Name | Error Description
Apache | Stack overflow in Apache Tomcat JK Connector
Eggdrop | Stack overflow in Eggdrop IRC bot
Lynx | Stack overflow in Lynx web browser
ProFTPD | Heap smashing attack on ProFTPD Server
Squid | Heap smashing attack on Squid proxy server

## Slide 35: Performance of Dataflow Sampling
ssh_receive
Chart: Maximum % Time in Analysis
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
 | 19.6739 | 16.8917 | 15.1671 | 13.0315 | 10.9794 | 8.8668 | 6.5111 | 4.1898 | 1.942 | 0.40485 | 0.17343
 | 19.7192 | 19.7192
Throughput with no analysis

## Slide 36: Accuracy with Background Tasks
ssh_receive running in background
Chart: Maximum % Time in Analysis
| 0.1 | 0.25 | 0.5 | 0.75 | 0.9
Apache | 0.1 | 0.7 | 2 | 11.7 | 65.3
Eggdrop | 8.6 | 20.4 | 53.3 | 62.8 | 89.4
Lynx | 8.8 | 15.7 | 38.2 | 46 | 90.2
ProFTPD | 11.8 | 13.2 | 28.4 | 53.9 | 89.7
Squid | 7.2 | 28 | 40 | 79.6 | 96.8

## Slide 37: BACKUP SLIDES

## Slide 38: Accuracy on Real Hardware
 | kmeans | facesim | ferret | freqmine | vips | x264 | streamcluster
W→W | 1/1 (100%) | 0/1 (0%) | - | - | 1/1 (100%) | - | 1/1 (100%)
R→W | - | 0/1 (0%) | 2/2 (100%) | 2/2 (100%) | 1/1 (100%) | 3/3 (100%) | 1/1 (100%)
W→R | - | 2/2 (100%) | 1/1 (100%) | 2/2 (100%) | 1/1 (100%) | 3/3/ (100%) | 1/1 (100%)
 | Spider Monkey-0 | Spider Monkey-1 | Spider Monkey-2 | NSPR-1 | Memcached-1 | Apache-1
W→W | 9/9 (100%) | 1/1 (100%) | 1/1 (100%) | 3/3 (100%) | - | 1/1 (100%)
R→W | 3/3 (100%) | - | 1/1 (100%) | 1/1 (100%) | 1/1 (100%) | 7/7 (100%)
W→R | 8/8 (100%) | 1/1 (100%) | 2/2 (100%) | 4/4 (100%) | - | 2/2 (100%)
 | kmeans | facesim | ferret | freqmine | vips | x264 | streamcluster
W→W | 1/1 (100%) | 0/1 (0%) | - | - | 1/1 (100%) | - | 1/1 (100%)
R→W | - | 0/1 (0%) | 2/2 (100%) | 2/2 (100%) | 1/1 (100%) | 3/3 (100%) | 1/1 (100%)
W→R | - | 2/2 (100%) | 1/1 (100%) | 2/2 (100%) | 1/1 (100%) | 3/3/ (100%) | 1/1 (100%)

## Slide 39: Width Test
Notes: In case the projector is clipping.